## Slide 1
MindSphere
Development training

## Slide 2: Agenda

## Slide 3: Day 1
Welcome
  Schedule, Agenda
  Introduction round
MindSphere Architecture
Northbound / Southbound
MindSphere IoT data model
Assets, AssetTypes, AspectTypes
Connectivity Overview
Infrastructure / MindSphere regions
MindSphere Plans, Sizes, Limits
Hierarchy & Inheritance
Dynamic vs static aspects
Metadata variables
Datatypes & Units
MindSphere onboarding
  Data mapping
  Timeseries
  Data in FleetManager
Short overview over APIs
  Location & Safety instructions

## Slide 4: Day 2
MindConnect API
  Authorization
  Tokens
Create an agent
  Node red
CloudFoundry
  Introduction
Setup environment
Postman
CloudFoundry CLI
Chrome
nodejs
  Data ingest
  Token renewal
  Org/Spaces/Users
  Buildpacks
  manifest.yml

## Slide 5: Day 3
Hello world
  Push application
  Register application
Asset Management
  API Overview
  Postman
Time Series
API Overview
Frontend/Backend app
Example dashboard app
  First API call
  Extend app with backend part
  Structure of Angular application
Postman
  Dashboard app
Dashboard app
Event Management
  API Overview
  Postman

## Slide 6
MindSphere
Overview & Architecture

## Slide 7: Architecture & API Learning Goals
MindSphere Architecture
MindSphere APIs
MindAccess Developer
How is MindSphere designed
&
how shall we develop applications for MindSphere?

## Slide 8: Continuously improve product and production The complete digital twin

## Slide 9: MindSphere is an end to end IoT operating system that enables a partner ecosystem Generic overview of different cloud models
Software as a Service: SaaS
Platform as a Service: PaaS
Infrastructure as a Service: Iaas
MindSphere
HW
Operating System
Virtual machine
Databases
Security
Apps / Services
Analytics
Agent based device connectivity
+
User managed
Provider managed
Notes: MindSphere ist mehr als IaaS PaaS SaaS

## Slide 10: MindSphere Siemens’ cloud-based, open IoT operating system
Applications
MindSphere applications provide asset transparency and analytical insights into machines, plants, fleets and systems
Open PaaS
MindSphere, the open PaaS, gives you scalable, global IoT connectivity and application development with native cloud accessibility
Connectivity
MindConnect connects products, plants, systems, machines, enterprise applications and legacy databases with a secured plug-and-play collection of Siemens and third-party products and equipment
Notes: MindSphere – the cloud-based, open IoT operating system – from Siemens, is a center piece of a powerful eco-system with data analytics and connectivity capabilities, tools for developers, applications and services. It helps to evaluate and utilize your data and to gain breakthrough insights. Drive the performance and optimization of your assets for maximized uptime.
On top of that, MindSphere also offers you the ability to immediately develop, deploy and run digital services, create own applications or even new business models.
Let me elaborate a little further on three aspects:
1. MindSphere applications -- enabling…
  Asset transparency and analytical insights, e.g., predictive maintenance,
  Subscription based pricing model,
  Fleet management.
2. MindSphere – the platform itself offers …
  Open interface for development of customer specific apps (MindApps),
  Various cloud infrastructures: Public, private or on-premise.
3. And MindConnect, which offers …
  Open standards Open standards (e.g. OPC UA) for connectivity (also to 3rd party products),
  Plug and play connection of Siemens products.
<CLICK>

## Slide 11: Connecting Assets to MindSphere: MindConnect
MindConnect IoT2040
MindConnect Nano
Software/Embedded Solutions
Hardware Solutions
MindConnect
MindConnect Integration (On-premise)
MindConnect Integration (Cloud)
MindConnect IoT Extension
MindConnect API / LIB
Notes: There are four ways to connect your assets:
With MindConnect MindSphere provides multiple, varied and easy-to-implement connectivity solutions to onboard a wide range of assets (Siemens and 3rd-party) in both brown- and greenfield: ---what is brownfield vs. greenfield?-----
We have two hardware devices to connect to MindSphere and two software/embedded solutions:
Focusing on brownfield installations, dedicated IoT Connectors like MindConnect Nano and MindConnect IoT2040, which provide plug and play connection of Siemens and 3rd party products thanks to communication via open standards like OPC UA
Both devices are similar, but IoT2040 is cheaper and has less performance, i.e. only up to 30 data points/second vs. up to 250 data points/second with MindConnect Nano
MindConnect FB 1500 is basically “a TIA (Totally Integrated Automation) Portal STEP7 library to extend the functions of the S7-1500 PLC” ---need to check data sheet for S7-1500 PLC----
MindConnect embedded agents in Siemens industrial products like SIMATIC and SINUMERIK focusing on greenfield projects ----belongs to which part?------
For every further product, including 3rd-party, MindConnect LIB, which enables self programming of connectivity modules by interacting with the MindSphere southbound APIs
Basically for MindConnect Lib there are only limits regards data sampling and data transfer, but the rest is up to your imagination
Currently MindConnect Lib is programmed only in “C”, but in the future other program languages will follow

## Slide 12: Connectivity @ MindSphere MindConnect Nano
MindConnect Nano is a device for collecting data using different protocols and transferring the data to MindSphere. The device supports transmission of data through a secure internet connection, to enable cloud-based applications and services. MindConnect Nano can only be used, according to the specific terms included in the datasheet, with MindSphere.
  Fast and easy connectivity of industrial machines and automation systems to MindSphere
  Data collection via standard industrial protocols
  Software Update Management – Always up to date
  Rugged design for maintenance-free, continuous operation
  Comprehensive security concept in accordance with applicable industry standards
  Up to 500MB local data buffer
  Siemens S7 (for collecting data from S7-3xx / S7-4xx / ET-200s PLCs);
  OPC UA (for collecting data from all data sources which can provide data via an OPC UA server); the MindSphere Nano supports data collection with Part 8 of the OPC UA specification (Data Access).
  Modbus (TCP and RTU)
Data reading cycle: Up to 250 data points / second
Data transfer cycle: Every 10 seconds
Description
Benefits
Supporting Protocols
Performance1
1) Performance upgrades follow

## Slide 13: Connectivity @ MindSphere MindConnect IoT2040
MindConnect IoT2040 is a device for collecting data using different protocols and transferring the data to MindSphere. The device supports transmission of data through a secure internet connection, to enable cloud-based applications and services. MindConnect IoT2040 can only be used, according to the specific terms included in the datasheet, with MindSphere.
  Fast and easy connectivity of industrial machines and automation systems to MindSphere
  Data collection via standard industrial protocols
  Software Update Management – Always up to date
  Rugged design for maintenance-free, continuous operation
  Comprehensive security concept in accordance with applicable industry standards
  Up to 500MB local data buffer
  Siemens S7 (for collecting data from S7-3xx / S7-4xx / ET-200s PLCs);
  OPC UA (for collecting data from all data sources which can provide data via an OPC UA server); the MindSphere Nano supports data collection with Part 8 of the OPC UA specification (Data Access).
  Modbus (TCP and RTU)
Data reading cycle: Up to 30 data points / second
Data transfer cycle: Every 10 seconds
Description
Benefits
Supporting Protocols
Performance1
1) Performance upgrades follow

## Slide 14: Connectivity @ MindSphere MindConnect API
MindConnect API is a firewall friendly RESTful API, which enables you to connect directly to MindSphere, without any dedicated hardware or software, directly from you process. It supports onboarding of your agent, secure internet connection with encrypted transmission of files, events, time series or custom specific data to MindSphere. It enable cloud-based applications and services.
  Enables connectivity for almost every asset (Siemens and 3rd party)
  Get Onboarding information for you asset via WEB UI
  Based on HTTPS
  Firewall-friendly communication via RESTful API
  Secure connectivity from an onsite device to the MindSphere platform
  Security profiles can be chosen from shared secret or RSA3072
  Transfer files, events, time series with multipart requests
  Data source configuration for time series possible from field level
Description
Benefits

## Slide 15: Connectivity @ MindSphere MindConnect LIB
MindConnect LIB is a “C” source code library, which enables customer to use connectivity to MindSphere within his own agents, e.g. embedded devices, programmable controllers or Linux/Windows PCs. It encapsulates the MindConnect API to those devices and handles the encrypted transmission of onsite data to MindSphere through a secure internet connection, to enable cloud-based applications and services.
  Enables connectivity for almost every asset (Siemens and 3rd party)
  Requires few system resources
  Secure connectivity from an onsite device to the MindSphere platform (e.g. authentication, encryption)
  Firewall-friendly communication via RESTful API
  Functions to onboard an agent, collect data and send it in a secure way to MindSphere
  File transfer functionality
  Eventing
  Local data buffering possible
  Depends on your local environment where the MindConnect LIB is going to be used, including interface to custom data parser at the platform backend for non timeseries data. Generally speaking: Any field protocol could be supported (with development into the Custom Agent)
Data reading cycle: Depending on performance of your underlying device, each use case, up to 250 data points / second
Data transfer cycle: Every 10 seconds
Description
Benefits
Supporting Protocols
Performance

## Slide 16: Connectivity @ MindSphere MindConnect IoT Extension1
MindConnect IoT Extension is a connectivity layer that expands the number of protocols that can communicate directly with MindSphere. Various field protocols are supported along with an increased range of hardware connectivity agents that create direct connection to assets in the production environment. Use the complete environment to create and manage agents and devices . MindConnect IoT Extension is included in MindAccess IoT Value Plan and Developer Plan with upgrades available for increases in data ingestion based on solution requirements.
  Expands MindSphere connectivity to all machines across the production floor
  Supports various field protocols and software agents
  Supports a wide range of hardware connectivity devices
  Provides a complete environment for agent development and device management
  Software Agents: MQTT Agent, Java Agent, C++ Agent
  Agent Development and SDKs: REST API, Web SDK, Web SDK for AngularJS
  Supported field protocols: HTTP/HTTPS, TCP, VNC, MQTT / MQTT+TLS, REST, SmartRest 1.0 / 2.0, OPC-UA, Modbus/RTU, Modbus/TCP, CAN bus, MMC, SPI, I2C, McASP, device specific protocols
  Compatible Devices: Adeunis LoRAWAN, BeagleBone Black, Cinterion Java Modules, CloudGate, Dell Edge Gateway, INSYS Smart Devices – INSYS OS, INSYS Smart Devices – icom OS, Janz Tec emPC A/RPI, Libelium-Mesehlium, Mbed u-blox C027, Meitrack, Netcomm, OPCUA Java Gateway, OWA3x, QuecLink, RaspberryPi, Red Lion RAM, SMARTBox, Robustel, SIGFOX, SMARTBox IO, SMARTBox Mini, TC3G, Telic, TinkerForge, Tixi
Description
Benefits
Scope2
1) Limited to time series values 2) Subject to change, please verify with your MindSphere sales representative

## Slide 17: Connectivity @ MindSphere MindConnect Integration1
MindConnect Integration is a secure way to connect multiple data systems into MindSphere. Using browser-based tools to graphically configure data value mapping, MindConnect Integration provides flexible tools to bring enterprise systems and data historians into context with MindSphere. MindConnect Integration offers different cloud and on premise connectors containing the knowledge of possible operations in each connected system. Starting from easy integration to complex data flows.
  Establish connectivity with existing databases and enterprise systems to open new avenues of analysis
  Connects multiple on site and on cloud data systems
  Provides browser based configuration tools for ease of integration
  Offers low maintenance and high flexibility
  Enables holistic analysis across company-wide data
  Facilitates better decision making and process optimization
  Cloud connectors: FTP(S), SOAP, REST, OData 2.0, OData 4.0, Alfabet, Cumulocity, Apps, BigQuery, Calendar, Cloud Storage, Contacts, Drive, Cloud Pub/Sub, Sheets,S3, SNS, SQS, Apache Solr, AvaTax, Concur, Coupa, Magento, Marketo, Microsoft Dynamics, NetSuite, SAP cloud, SAP Hana Marketing Cloud, Salesforce, Salesforce CRM, ServiceNow, Slack, StrikeIron, SuccesFactors, SugarCRM, Zendesk
  On premise connectors: Ariba, OnRamp, LotusNotes, OFTP, Oracle, PeopleSoft, Remedy, SAP, SAP XI, Siebel, AS/400, JavaBeans, JDBC, Apache HIVE, MongoDB, Cassandra, HDFS, Apache Impala, Apache WebSphereMQ, Tuxedo, MSMQ, Apache Kafka
Description
Benefits
Scope2
1) Limited to time series values 2) Subject to change, please verify with your MindSphere sales representative

## Slide 18: Connectivity @ MindSphere MindConnect Edge Analytics2
  Solution for preprocessing and sending data to MindSphere. It performs signal pre-processing on the edge of the network using X-Tools technology before sending the processed data to MindSphere. Once the data is in, MindSphere detects possible damage to machinery. Flexible analytics help drive root-cause analysis and predictive maintenance to proactively manage downtime of assets.
  Edge analytics through data preprocessing
  Recording of high dynamic signals from a variety of data sources with sampling rates up to 50 kHz
  Local data buffering in memory for analysis then send it to MindSphere for long-term archiving
  Usage of seven predefined KPI calculations: RMS Velocity, Peak-Peak Velocity, Zero-Peak Velocity, RMS Acceleration, Peak-Peak Acceleration, Zero-Peak Acceleration, Crest Factor
  Improved asset availability through predictive maintenance
  MindAccess IoT Value Plan (for productive use) or MindAccess DevOps Plan (for test with self-developed apps purposes)
  MindConnect Nano
  MindConnect Edge Analytics Engine
  MindConnect Edge Analytics Engineer
The MindConnect Edge Analytics Engine provides high frequency (max. 50 kHz) data collection of up to 5 data points1 through MindConnect Nano. Expansion of data points can be purchased in the near future with MindConnect Edge Analytics Engine +50 or MindConnect Edge Analytics Engine +300 (not available yet)
Description
Benefits
Prerequisites
Performance
1) Currently 1 SIPLUS SM 1281 p. MindConnect Nano supported only 2) Release upcoming for MindSphere on Azure
Supporting Protocols

## Slide 19: System architecture Architecture overview (simplified)
Customer plant
Machine
Agent
Internet (https)
MindSphere Gateway (Northbound)
MindSphere Gateway (Southbound)
User
Postgre SQL
Mongo DB
Backing services
Cloud Foundry
…
Orgs & Spaces
Analytics Services
Identity Access Management Services
Asset Management Service
NoSQL database
Aggregates
Object storage
IoT API
Tenant separation, data groups
Big data store
…
Internet (https)

## Slide 20: System architecture Architecture overview
Internet (https)
NoSQL database
Aggregates
DynamoDB
Object storage
Redis
Rabbit MQ
Postgre SQL
Mongo
Customer plant
Machine
Agent
Internet (https)
Connectivity
IAM services
IoT API
Tenant separation, data groups
JWT
provider
Checks (CF broker)
MDSP Gateway
Authentication → adds JWT to call
Advanced svcs
JWT check
Integration to Webkey
ELK
Log
Third party app/svc
Aurora
Kinesis
S3
SQS/SNS
Dynamo DB
Checks
JWT check
…
User
3rd party developer
3rd party provider
Siemens user
Custom auth
JWT check
Provider accounts
Big data store
Backing services
Cloud Foundry
space
Cloud infrastructure provider account
Third party app/svc
JWT check

## Slide 21: MindSphere Example Launchpad

## Slide 22: MindSphere API Scalable Application Development
  API: Application Programming Interface
  A set of subroutines, protocols and tools to build application software = Building blocks that make the application development fast and easy
  APIs optimized for industrial IoT application development
  Long term stability for min. 2 years to fulfill industrial needs (long product lifecycles)
  API versioning and backward compatibility
  Continuous demand-based functionality extension
Develop your own applications running on MindSphere

## Slide 23: MindSphere API
6_84 95_84 34_84 37_84
MindSphere API
Data Flow Engine
Notification Service
Anomaly Detection
Signal Validation
KPI Calculation
Trend Prediction
Event Analytics
Context Delivery Serv.
Signal Calculation
Asset Management
Agent Management
MindConnect API
Identity/Access Mgmt.
Time Series Service
Event Management
Model Management
TS Aggregate Service
MindSphere API
File Service

## Slide 24: MindSphere Data Centers
  For MindSphere on AWS currently we use the AWS data center cluster in Germany for data storage. MindSphere on AWS tenant URLs appear as
  https://ACCOUNTNAME.eu1.mindsphere.io
  For MindSphere on Azure currently we use the Microsoft Azure data center cluster in the Netherlands for data storage. MindSphere on Azure tenant URLs appear as
  https://ACCOUNTNAME.eu2.mindsphere.io
  AWS and Microsoft do not have access to any customer data stored in MindSphere.
  As part of the further development of MindSphere, the data center coverage will be extended. At a first stage in EU and US:
    Adhering to security and data privacy rules
    Following export regulations

## Slide 25: Introducing Content and Context of MindSphere
Developer
Operator
LP
Connect
User
Store

## Slide 26: Introducing Content and Context of MindSphere
LP
MindConnect
MindAccess IoT Value Plan
MindSphere Store
MindAccess Developer
MindAccess Operator

## Slide 27: Add value and bridge the gap between multiple roles
Developers
Develop applications
Build applications
Test applications
Publish applications
Developer cockpit
Operators
Operate applications via SaaS
Manage and offer application
Manage & Monitor Users and Usage
Operator cockpit
Users
Use applications
Ability to access device data
Visualize trends
Launchpad
MindSphere provides a single source of truth for all roles enabling operational alignment and collaboration

## Slide 28: MindSphere Offering Structure
MindAccess IoT Value Plan
Use MindSphere applications based on ingested data – without development know-how
MindAccess DevOps Plan
MindAccess Developer Plan
Develop applications on a test system
MindAccess Operator Plan
Operate applications on a productive system and offer them via MindSphere Store
Customers need to order at least one of the base plans…
Data ingest & storage
Productive tenant
Asset management
User management
Fleet Manager
MindConnect IoT Extension
Access to MindSphere Store
Cloud Foundry developer space
Developer test tenant
Basic APIs including analytics
Test asset and user management
Developer data storage
Developer cockpit
Cloud Foundry productive space
Basic APIs including analytics
Operator cockpit / access to MindSphere Store

## Slide 29: MindAccess IoT Value Plan Resources Overview
IoT Value Plan | S small customers/ OEMs | M worldwide installed base | L big international plants
No. of users / Subtenants4) | 50 / 10 | 150 / 40 | 500 / 80
Agents onboarded | 10 | 25 | 100
Assets included (types/ instances) | 5 / 50 | 10 / 250 | 50 / 1,000
Data ingest rate3) (time series) | 2 KB/s | 10 KB/s | 100 KB/s
Data storage time series (cold storage) | 60 GB | 300 GB | 3 TB
Data ingest via IoT extensions2), monthly | 5 GB | 5 GB | 5 GB
File storage | 50 GB | 100 GB | 500 GB
User Management |  |  | 
Asset Management |  |  | 
Productive Tenant |  |  | 
Access to MindSphere Store |  |  | 
Fleet Manager Basic incl. rules and events1) |  |  | 
1) Limited use of rules & events. one active concurrent rule included in all plan sizes; upgrade available 2) Part of overall data ingest 3) Based on no. of assets, no. of variables per asset, size per variable, read cycle interval and sending frequency; exemplary use case for M size: 200 assets with 10 variables each sending frequency 10s, 20 assets with 100 variables each sending frequency 10s, etc. (assumptions: 50 Bytes per variable including overhead – float from MindConnect Nano/ IoT2040 or S7-FB, read cycle equals sending frequency) 4) Release upcoming for MindSphere on Azure

## Slide 30: MindAccess Developer Plan Resources Overview
Developer Plan (Cloud Foundry) | S | M | L
Test & development resources (RAM) | 2 GB | 10 GB | 20 GB
Cloud Foundry development space |  |  | 
Highly available system (several availability zones) |  |  | 
Development tenant |  |  | 
Developer cockpit |  |  | 
Fleet Manager Basic incl. rules and events3) |  |  | 
MindSphere APIs1) |  |  | 
Unlimited no. of routes |  |  | 
Included backing service instances (plan XS) | 2 | 4 | 6
Number of developers/ test users | 10 | 50 | 100
Connected assets types/ instances/ agents2) | 5 / 20 / 1 | 25 / 100 / 5 | 50 / 200 / 10
Outbound traffic, monthly4 | 60 GB | 300 GB | 600 GB
New app transfers to operations system, monthly | 1 | 5 | 10
Developer resources | Documentation, Getting Started, Community |  | 
Supported Build Packs | Go, Java, Node.js, .Net core, PHP, Python, Ruby, Static File (s. Product Sheet for always up-to-date information) |  | 
Comprehensive set of MindSphere APIs e.g. analytics, notification service, context delivery service; number of calls limited, higher packages include more calls; upgrades available
Inbound traffic and respective storage for testing included (according to data sheet)
Limited use of rules & events; one active concurrent rule included in all plan sizes; upgrade available
Release upcoming for MindSphere on Azure

## Slide 31: MindAccess Operator Plan Resources Overview
Operator Plan (Cloud Foundry) | S | M | L
Productive system resources (RAM) | 2 GB | 10 GB | 20 GB
Cloud Foundry productive space |  |  | 
Highly available system (several availability zones) |  |  | 
Productive tenant for monitoring & support |  |  | 
Operator cockpit w/ access to MindSphere Store |  |  | 
Fleet Manager Basic incl. rules and events3) |  |  | 
MindSphere APIs1) |  |  | 
Unlimited no. of routes |  |  | 
Number of operator users | 5 | 10 | 25
Connected assets types/ instances/ agents2) | 5 / 20 / 1 | 25 / 100 / 5 | 50 / 200 / 10
Outbound traffic, monthly4) | 60 GB | 300 GB | 600 GB
New uploads to MindSphere Store, monthly | 1 | 5 | 10
Operator Resources | Documentation, Getting Started, Seller Guide |  | 
Supported Build Packs | Go, Java, Node.js, .Net core, PHP, Python, Ruby, Static File (s. Product Sheet for always up-to-date information) |  | 
Comprehensive set of MindSphere APIs e.g. analytics, notification service, context delivery service; number of calls limited, higher packages include more calls; upgrades available
Inbound traffic and respective storage for testing included (according to data sheet)
Limited use of rules & events. one active concurrent rule included in all plan sizes, upgrade available
Release upcoming for MindSphere on Azure

## Slide 32: MindSphere General Details
MindSphere
Multitenant System
Strict data separation between tenants
Data access only for the assigned owner of the tenant (=data owner)
Hierarchical tenant system ("OEM Usecase")
Tenant
Subtenant
Data A
Data B
Tenant A App
Tenant B App
Tenant A
Subtenant A1
Subtenant A2

## Slide 33: Application and tenant management Subtenant access
  Subtenants cannot see/access other subtenants, nor are they allowed to see data of the tenant; they cannot create new assets or asset types
  Subtenants may only change the IP address of a device to accommodate the new location of the device
  A tenant can delete his subtenants
  Dedicated endpoint for subtenant management as part of the existing user and group management service

## Slide 34: Application Lifecycle How to get an App from the Developer to the User?
Local Environ-ment
Dev. Test System
Operator
Developer
User
Developer Cockpit
LaunchPad
Storefront & Backend
(MindSphere Store)
Operator Cockpit
App exchange repository
Live System
(Productive Environment)
Operator Tenant
Secure data transfer between User Tenant and provisioned Application
Prerequisite
CF CLI
App Onboarding
Setup Route
Store onboarding
App Provisioning for BU Apps
Manual App Provisioning
CF Push
Process started by Operator
Process started by Developer
- simplified -
Subscription, notification for 3rd party Apps
Deploy
Download
CLI = Command Line Interpreter

## Slide 35: How to Use MindSphere Platform? Develop and Operate Apps
MindAccess DevOps Plan
MindAccess Developer Plan
Develop applications on a test system
Developer tenant
Test App 1
Test App 2
Developer e.g. Atos, Siemens BU,
individual developer
Data ingest for test purpose
Developer Organization
MindAccess Operator Plan
Operate applications on a productive system and offer via MindSphere Store
App 1
App 2
Productive Organization
Apps from one or several developers
Operator/ provider e.g. Atos, Siemens BU
2
Developer transfers App to operations system
3
3
Operator/ provider operates App
Exemplary user journey:
Develop on your local developer environment (e.g. Eclipse) using MindSphere API Documentation
2
1
Developer pushes App to development system
1
MindSphere Store
4
4
Operator/ provider creates Offering in MindSphere Store
Notes: --------------------------------------
What is the right solution for whom?
Describe when only Dev Plan is necessary, when Ops Plan and when both

## Slide 36: How to Use MindSphere Platform? Consume App
MindAccess DevOps Plan
MindAccess Operator Plan
Operate applications on a productive system and offer via MindSphere Store
App 1
App 2
Productive Organization
Apps from one or several developers
Operator/ provider
3
4
End user requests App in MindSphere Store
5a
Route from acquired App to tenant of end user established
5b
End user uses App based on ingested data
Exemplary user journey:
MindAccess IoT Value Plan
Use MindSphere applications based on ingested data – without development knowhow
End user (end customer or OEM)
Productive tenant1)
Access to Apps from one or several operators/ providers e.g. requested via MindSphere Store
App 1
3
Operator/ provider uploads App to MindSphere Store
4
Data ingest
5a
MindAccess IoT Value Plan
Use MindSphere applications based on ingested data – without development knowhow
End user (end customer or OEM)
Productive tenant1)
App 2
4
Data ingest
Access to Apps from one or several operators/ providers e.g. requested via MindSphere Store
5a
5b
5b
Notes: One operator servers mutltiple apps for multiple IoT Value Plans.
All data is stored in the IoT Value Plan (customer)

## Slide 37: MindSphere Consume Multitenancy App
MindAccess DevOps Plan
MindAccess Operator Plan
Operate applications on a productive system and offer via MindSphere Store
App 1
Productive Organization
Apps from one or several developers
Operator/ provider
3
4
End user buys App in MindSphere Store
5a
Route from acquired App to tenant of end user established
5b
End user uses App based on ingested data
Exemplary user journey:
MindAccess IoT Value Plan
Use MindSphere applications based on ingested data – without development knowhow
End user (end customer or OEM)
Productive tenant1)
Access to Apps from one or several operators/ providers e.g. requested via MindSphere Store
App 1
3
Operator/ provider uploads App to MindSphere Store
4
Data ingest
5a
MindAccess IoT Value Plan
Use MindSphere applications based on ingested data – without development knowhow
End user (end customer or OEM)
Productive tenant1)
App 1
4
Data ingest
Access to Apps from one or several operators/ providers e.g. requested via MindSphere Store
5a
5b
5b
Notes: One operator servers the same app for multiple IoT Value Plans.
All data is stored in the IoT Value Plan (customer)

## Slide 38: How to Use MindSphere Platform? OEM Use case
MindAccess DevOps Plan
MindAccess Operator Plan
Operate applications on a productive system and offer via MindSphere Store
App 1
App 2
Productive Organization
Apps from one or several developers
Operator/ provider
3
4
Customer receives access right to
App from OEM
5a
Route from App to customer established
5b
Customer uses App based on ingested data
Exemplary user journey:
MindAccess IoT Value Plan
Use MindSphere applications based on ingested data – without development knowhow
End user (end customer or OEM)
3
OEM operates an App in
MindSphere
5b
Customer (C1)
Use MindSphere applications based on ingested data – without development knowhow
End user (end customer of OEM)1)
App 1
Customer (C2)
Use MindSphere applications based on ingested data – without development knowhow
End user (end customer of OEM) 1)
App 2
Data ingest
Productive tenant1)
C1
C2
4
4
5b
5b

## Slide 39: Architecture & API Summary
How is MindSphere designed?
As an open platform as a service (PaaS) for scalable, global IoT connectivity and application development.
How shall we develop applications for MindSphere?
By getting MindAccess Developer plan (S, M, L), we can start using 18 different APIs to make the application development easy and fast.

## Slide 40
MindSphere
IoT data model

## Slide 41: Architecture & API Learning Goals
Objective
Concept
Brewery Use-Case
How does the IoT data model in MindSphere work?

## Slide 42: What do we want to do?

## Slide 43: How can we do this?
Virtual Asset
Physical Asset
(Agent)
Aspects
Data
Source
Data
Point
Variable

## Slide 44: Our Use Case – Brewery Architecture
basement
pump
beer tank
valve
fluid-flow meter
bottling

## Slide 45: Our Use Case – Brewery Architecture
basement
pump
beer tank
valve
fluid-flow meter
obstruction in pipe or closed valve
bottling

## Slide 46: Our Use Case – Brewery Measured Data Points
beer tank
fluid-flow
pressure before pump
pressure behind pump
motor current
temperature of stuffing box
bottling
basement

## Slide 47: Our Use Case – Brewery Measured Data Points
DataPoint | DataType | Unit
Motor_Current | INT | A
Fluid_Flow | DOUBLE | m3/h
Temperature | DOUBLE | C
Pressure_In | DOUBLE | hPa
Pressure_Out | DOUBLE | hPa

## Slide 48: MindSphere data types
Type | Description
BOOLEAN | Variable that stores one of two possible values: true (TRUE) or false (FALSE)
INT | Variable that stores an integer up to 32 bits.
LONG | Variable that stores an integer up to 64 bits.
DOUBLE | Variable that stores a decimal up to 64 bits.
STRING | Variable that stores a string up to 255 characters (usually text).
BIG_STRING | Variable that stores a string up to 100,000 characters.
TIMESTAMP | Variable that stores a time value

## Slide 49: Asset structure
MyPump1: PumpType
MyPump2: PumpType
PumpType
<<AssetType>>
PumpMetrics
<<AspectType>>
MotorCurrent
<<Variable>>
Passage
<<Variable>>
Metrics
Virtual Asset
Physical Asset
(Agent)
Aspects
Data
Source
Data
Point
Variable
Temperature
<<Variable>>

## Slide 50: Asset Manager Demo 1 Basic usage

## Slide 51: Exercise 1
Task: Create the basic asset structure for our pump usecase
Create an aspect type for your pump with 3 variables:
Create an asset type for your pump referencing your previously created aspect type.
Create an asset based on your previously created asset type
DataPoint | DataType | Unit
MotorCurrent | INT | A
FluidFlow | DOUBLE | m3/h
Temperature | DOUBLE | C

## Slide 52: Aspect type reuse
MyPump1: PumpType
MyPump2: PumpType
PumpType
<<AssetType>>
PumpMetrics
<<AspectType>>
MotorCurrent
<<Variable>>
Temperature
<<Variable>>
PressureIn
PressureMetrics
<<AspectType>>
PressureMetrics
<<AspectType>>
Pressure
<<Variable>>
FluidFlow
<<Variable>>
Metrics
PressureOut
Pressure
<<Variable>>

## Slide 53: Static aspects
Dynamic aspects  Timeseries data
Static aspects  Non timeseries data
Examples
Current state of machine
Online / Offline status
Last error code

## Slide 54: Asset data & Asset properties
General data fields for assets:
Name
Description
TimeZone
Location
  Street
  Postal code
  City
  Country
  Region
  Latitude & Longitude
Addition fields can be created as so called "Variables"
For example:
Serial Number
Installation date

## Slide 55: Asset Manager Demo 2 Aspect type reuse & static aspects

## Slide 56: Exercise 2
Task: Enhance your data structure
Create an aspect type for pressure (DOUBLE / hPa)
Add this pressure aspect to your existing asset type twice as PressureIn and PressureOut
Create a static aspect type with two variables: isRunning OverallVolume
Add this static aspect type to your existing asset type
Add two property variables to your asset type and add some dummy data to them: SapInventoryNumber InstallationDate

## Slide 57: Asset hierarchy
academy2
<<core.basicenterprise>>
BreweryKarlsruhe
<<core.basicarea>>
Building1
<<core.basicsite>>
MyPump1
<<academy2.PumpType>>
Building2
<<core.basicsite>>
MyPump2
<<academy2.PumpType>>
MyPump3
<<academy2.PumpType>>

## Slide 58: Asset type inheritance
PumpType
MotorCurrent: Double
Temperature: Double
MyPump1: PumpType
MotorCurrent: 35
Temperature: 27
<<instance.of>>
ExtendedPumpType
Vibration: Double
MyExtendedPump:
ExtendedPumpType
MotorCurrent: 88
Temperature: 33
Vibration: 200
<<instance.of>>

## Slide 59: Asset Manager Demo 3 Asset hierarchy & asset type inheritance

## Slide 60: Exercise 3
Task: Create a brewery structure
Create a hierarchy asset under the main asset for the current training (named by the trainer)
Move your existing pump asset in your hierarchy
Create a second pump asset and another hierarchy asset

## Slide 61: Big picture
Virtual Asset
Physical Asset
(Agent)
Aspects
Data
Source
Data
Point
Variable

## Slide 62: Pump data access
OPC UA
Server

## Slide 63: Data mapping
Asset Core Type
Physical Asset
Data Source
Data Point 1
Data Point 2
Data Point 3
Asset Type
Virtual Asset
Aspect
Variable 1
Variable 2
Variable 3
devices
Sensor Data 1
Sensor Data 2
Sensor Data 3

## Slide 64: Complex mapping
Physical Assets
Virtual Assets
Motor 1
DataPoint1
DataPoint2
Sensor
DataPoint6
Motor 1
Variable1
Variable2
Motor 2
DataPoint3
DataPoint4
DataPoint5
Line 1
Variable1
Variable3
Variable4
Variable5
Variable6

## Slide 65: Asset Manager Demo 4 MindConnect Nano configuration & data mapping

## Slide 66: Exercise 4
Task: Map our live pump data to your asset
Search for the MindConnect Nano in Asset Manager (name and location provided by trainer)
Map the following 5 datapoints to your pump asset:
Notes: The MindConnect Nano with our Live pump data is here:
academy2 => X-Tools & MCEA Training => Erlangen_Lab_Demos => MCEA_MCN_H2950627

## Slide 67: Data in Fleet Manager

## Slide 68: MindSphere Iot data model API structure
AssetType
1
1..N
Asset
1
0..N
AspectType (dynamic or static)
parentTypeId
parentId
Variable
Variable
typeId
1..N
1..N
1..N
Overview

## Slide 69: Iot data model Summary
What does the IoT data model looks like in MindSphere?
The IoT data model is based on a virtual and a physical asset.

## Slide 70
MindConnect API

## Slide 71: MindConnect API Learning Goals
MindConnect API
Overview of MindConnect API

## Slide 72: MindConnect API Idea
The MindConnect Service exposes an API that enables shop floor devices to send data securely and reliable to MindSphere. It opens the MindSphere platform to custom applications to collect and send data which shall be stored and used by applications in the cloud.
The MindConnect Service enables the development of custom data collectors, also referred as custom agents. This software applications act as data sources that upload the collected data into the MindSphere.
Notes: S7comm (S7 Communication) is a Siemens proprietary protocol that runs between programmable logic controllers (PLCs) of the Siemens S7-300/400 family.
It is used for PLC programming, exchanging data between PLCs, accessing PLC data from SCADA (supervisory control and data acquisition) systems and diagnostic purposes

## Slide 73: MindConnect API Access
The custom agent needs a field side network infrastructure to forward and route outbound HTTPs requests to the Internet.
MindConnect supports multiple agent device classes: strong hardware platforms as well as resource constrained devices. All target agent platforms must comply to the following minimum requirements:
HTTP processing
TLS
JSON parsing
JSON Web Token (JWT) generation
HMAC generation (preferably SHA2 based hashing)
Notes: S7comm (S7 Communication) is a Siemens proprietary protocol that runs between programmable logic controllers (PLCs) of the Siemens S7-300/400 family.
It is used for PLC programming, exchanging data between PLCs, accessing PLC data from SCADA (supervisory control and data acquisition) systems and diagnostic purposes

## Slide 74: MindConnect API General Workflow
Provisioning an Agent
Acquiring Boarding Configuration
Onboarding the Agent
Acquiring Access Token
Configuring Data Source
Consuming Exchange Services

## Slide 75: MindConnect API Prepare the Type and Agent Asset
In order to create an agent an Agent Asset needs to be created with a type derived from core.basicagent. When the agent should communicate with MindSphere through MindConnect Library, or directly through MindConnect API, its Agent Asset should be created having a type core.mclib, or a type derived from it.
Provisioning an Agent
Onboarding Agent
Create Data Point Mapping
Exchange Data
Acquiring Access Token
DataSource Configuration
Boarding Configuration

## Slide 76: MindConnect API Hands-On Exercise 2: Device Asset
Create Aspect, Type and Device Asset
Provisioning an Agent
Onboarding Agent
Create Data Point Mapping
Exchange Data
Acquiring Access Token
DataSource Configuration
Boarding Configuration
Hands-on

## Slide 77: MindConnect API Hands-On Exercise 3: Agent Asset and Boarding Information
Hands-on
Task 1: Create Agent Asset and generate boarding information
Provisioning an Agent
Onboarding Agent
Create Data Point Mapping
Exchange Data
Acquiring Access Token
DataSource Configuration
Boarding Configuration

## Slide 78: MindConnect API Boarding Configuration
After agent creation, agent needs to acquire boarding configuration in order to board to MindSphere. If agent is not boarded, it cannot use any of the services offered by Mindsphere. Boarding functionality is provided by Boarding endpoint.
Clicking on Generate onboarding key within Asset Manager returns following information:
Boarding Configuration
Acquiring an Access Token
Create Data Point Mapping
Exchange Data
DataSource Configuration
Provisioning an Agent
Onboarding the Agent
Parameter | Description | Remarks
baseUrl | Holds the southgate url | 
iat | Initial Access Token, A JSON Web Token that is being signed by the AgentIAM, required to do initial registration. | IAT are subject to expiration and by default they have 7 days of validity, if IAT expired; Agent needs to call this endpoint to acquire a new configuration.
clientCredentialProfile | Agents security profile, set during provisioning step. | RSA_3072, SHARED_SECRET
clientId | Agent Id | 
tenant | Agents tenant | 
expiration | Holds IAT expiration time | Default value is 7 days

## Slide 79: MindConnect API Boarding Configuration
Boarding Configuration
Acquiring an Access Token
Create Data Point Mapping
Exchange Data
DataSource Configuration
Provisioning an Agent
Onboarding the Agent
{
"content": {
"baseUrl": "https://southgate.eu-central.mindsphere.io",
"iat": "eyJhbGciOiJSUzI1NiIsInR5cCI6IkpXVCJ9.eyJpc3MiOiJTQ0kiLCJzdWIiOiJ0ZXN0LWFnZW50IiwiYXVkIjpbIkFJQU0iXSwiaWF0IjoxNTEzNjA3NjQ3LCJuYmYiOjE1MTM2MDc2NDcsImV4cCI6MTUxNDIxMjQ0NywianRpIjoiODBkNGViYTAtZTQwMC0xMWU3LTlmMDYtM2QzOTg3NTQ1MjNjIiwic2NvcGUiOlsiSUFUIl0sInRlbmFudCI6InRlc3QtdGVuYW50IiwiY2xpZW50X2NyZWRlbnRpYWxzX3Byb2ZpbGUiOlsiUlNBXzMwNzIiXSwic2NoZW1hcyI6WyJ1cm46c2llbWVuczptaW5kc3BoZXJlOnYxIl19.F/C44dH0orAVrKXDxcdGTgDFGsYzxOLR84j49S1qQMcX4GKq0HGfN7mm9N2tAUo8+z9ISRIW+D/n81uioF4ro+cyjGFbstatsRVH8hFFbZe4WcSChBHpwmA9IBOL0iFo/8C/7FppjhmHnlJNTQrfdkPJbtgQljtlY46BqW2pKp3wPUPJb21nLhVwMv1AiAbISg17FazhzuV7n12pJxdtpEB+mYZZe16P9amW217iyaDyRZ0+UhldHyKYwX0in5SpvJ1gzFlhMNwYWhG8zk6EJ8OYY49OhTYLHtvoEm8IIxarPWWmMztwrEXvNvQi6svZ1NCcgbkuSTwdEyJDzPqmbw==",
"clientCredentialProfile": [
"SHARED_SECRET"
],
"clientId": "5fa51b64-dce2-11e7-9296-cec278b6b50a",
"tenant": "6e70640a-dce2-11e7-9296-cec278b6b50a"
},
"expiration": "2017-12-18T14:04:01.076Z"
}

## Slide 80: Onboarding and Communication Use Case Flow
Initialization (IAT)
ErrorCode (OK / FAIL)
Onboard
Register (IAT)
Response with RAT + Client Secret
ErrorCode (OK / FAIL)
Key Rotation
Register (RAT)
Response with new RAT +Client Secret
ErrorCode (OK / FAIL)
MindConnect API
Exchange (AAT)
Exchange (AAT)
Response
ErrorCode (OK / FAIL)
Acquire Access Token
Request Token
Response with AAT
ErrorCode (OK / FAIL)

## Slide 81: JWT
Boarding Configuration
Acquiring an Access Token
Create Data Point Mapping
Exchange Data
DataSource Configuration
Provisioning an Agent
Onboarding the Agent
Notes: https://stackoverflow.com/questions/4657416/difference-between-encoding-and-encryption
https://medium.com/vandium-software/5-easy-steps-to-understanding-json-web-tokens-jwt-1164c0adfcec
In this example, the user first signs into the authentication server using the authentication server’s login system (e.g. username and password, Facebook login, Google login, etc). The authentication server then creates the JWT and sends it to the user. When the user makes API calls to the application, the user passes the JWT along with the API call. In this setup, the application server would be configured to verify that the incoming JWT are created by the authentication server (the verification process will be explained in more detail later). So, when the user makes API calls with the attached JWT, the application can use the JWT to verify that the API call is coming from an authenticated user.
Now, the JWT itself, and how it’s constructed and verified, will be examined in more depth.
Step 1. Create the HEADER
The header component of the JWT contains information about how the JWT signature should be computed. The header is a JSON object in the following format:
In this JSON, the value of the “typ” key specifies that the object is a JWT, and the value of the “alg” key specifies which hashing algorithm is being used to create the JWT signature component. In our example, we’re using the HMAC-SHA256 algorithm, a hashing algorithm that uses a secret key, to compute the signature (discussed in more detail in step 3).
Step 2. Create the PAYLOAD
The payload component of the JWT is the data that‘s stored inside the JWT (this data is also referred to as the “claims” of the JWT). In our example, the authentication server creates a JWT with the user information stored inside of it, specifically the user ID.
The data inside the payload is referred to as the “claims” of the token.In our example, we are only putting one claim into the payload. You can put as many claims as you like. There are several different standard claims for the JWT payload, such as “iss” the issuer, “sub” the subject, and “exp” the expiration time. These fields can be useful when creating JWT, but they are optional. See the wikipedia page on JWT for a more detailed list of JWT standard fields.
Keep in mind that the size of the data will affect the overall size of the JWT, this generally isn’t an issue but having excessively large JWT may negatively affect performance and cause latency.
Step 3. Create the SIGNATURE
The signature is computed using the following pseudo code:
// signature algorithmdata = base64urlEncode( header ) + “.” + base64urlEncode( payload )signature = Hash( data, secret );What this algorithm does is base64url encodes the header and the payload created in steps 1 and 2. The algorithm then joins the resulting encoded strings together with a period (.) in between them. In our pseudo code, this joined string is assigned to data. To get the JWT signature, the data string is hashed with the secret key using the hashing algorithm specified in the JWT header.
In our example, both the header, and the payload are base64url encoded as:
// header eyJ0eXAiOiJKV1QiLCJhbGciOiJIUzI1NiJ9// payload eyJ1c2VySWQiOiJiMDhmODZhZi0zNWRhLTQ4ZjItOGZhYi1jZWYzOTA0NjYwYmQifQThen, using the joined encoded header and payload, and applying the specified signature algorithm(HS256) on the data string with the secret key set as the string “secret”, we get the following JWT Signature:
// signature-xN_h82PHVTCMA9vdoHrcZxH-x5mb11y1537t3rGzcMStep 4. Put All Three JWT Components Together
Now that we have created all three components, we can create the JWT. Remembering the header.payload.signature structure of the JWT, we simply need to combine the components, with periods (.) separating them. We use the base64url encoded versions of the header and of the payload, and the signature we arrived at in step 3.
// JWT Token eyJ0eXAiOiJKV1QiLCJhbGciOiJIUzI1NiJ9.eyJ1c2VySWQiOiJiMDhmODZhZi0zNWRhLTQ4ZjItOGZhYi1jZWYzOTA0NjYwYmQifQ.-xN_h82PHVTCMA9vdoHrcZxH-x5mb11y1537t3rGzcMYou can try creating your own JWT through your browser at jwt.io.
Going back to our example, the authentication server can now send this JWT to the user.
How does JWT protect our data?
It is important to understand that the purpose of using JWT is NOT to hide or obscure data in any way. The reason why JWT are used is to prove that the sent data was actually created by an authentic source.
As demonstrated in the previous steps, the data inside a JWT is encoded and signed, not encrypted. The purpose of encoding data is to transform the data’s structure. Signing data allows the data receiver to verify the authenticity of the source of the data. So encoding and signing data does NOT secure the data. On the other hand, the main purpose of encryption is to secure the data and to prevent unauthorized access. For a more detailed explanation of the differences between encoding and encryption, and also for more information on how hashing works, see this article.
Since JWT are signed and encoded only, and since JWT are not encrypted, JWT do not guarantee any security for sensitive data.Step 5. Verifying the JWT
In our simple 3 entity example, we are using a JWT that is signed by the HS256 algorithm where only the authentication server and the application server know the secret key. The application server receives the secret key from the authentication server when the application sets up its authentication process. Since the application knows the secret key, when the user makes a JWT-attached API call to the application, the application can perform the same signature algorithm as in Step 3 on the JWT. The application can then verify that the signature obtained from it’s own hashing operation matches the signature on the JWT itself (i.e. it matches the JWT signature created by the authentication server). If the signatures match, then that means the JWT is valid which indicates that the API call is coming from an authentic source. Otherwise, if the signatures don’t match, then it means that the received JWT is invalid, which may be an indicator of a potential attack on the application. So by verifying the JWT, the application adds a layer of trust between itself and the user.
In Conclusion
We went over what JWT are, how they are created and validated, and how they can be used to ensure trust between an application and its users. This is a starting point for understanding the fundamentals of JWT and why they are useful. JWT are just one piece of the puzzle in ensuring trust and security in your application.
It should be noted that the JWT authentication setup described in this article is using a symmetric key algorithm (HS256). You can also set up your JWT authentication in a similar way except using an asymmetric algorithm (such as RS256) where the authentication server has a secret key, and the application server has a public key. Check out this Stack Overflow question for a detailed breakdown of the differences between using symmetric and asymmetric algorithms.
It should also be noted that JWT should be sent over HTTPS connections (not HTTP). Having HTTPS helps prevents unauthorized users from stealing the sent JWT by making it so that the communication between the servers and the user cannot be intercepted . Also having an expiration in your JWT payload, a short one in particular, is important so that if old JWT ever get compromised, they will be considered invalid and can no longer be used.
If you enjoyed this article and are writing handlers for AWS Lambda and are implementing JWT, please check out our project: Vandium

## Slide 82: JWT
Boarding Configuration
Acquiring an Access Token
Create Data Point Mapping
Exchange Data
DataSource Configuration
Provisioning an Agent
Onboarding the Agent
From: https://developer.mindsphere.io/howto/howto-agent-onboard.html
continued on next slide
Notes: https://stackoverflow.com/questions/4657416/difference-between-encoding-and-encryption
https://medium.com/vandium-software/5-easy-steps-to-understanding-json-web-tokens-jwt-1164c0adfcec
In this example, the user first signs into the authentication server using the authentication server’s login system (e.g. username and password, Facebook login, Google login, etc). The authentication server then creates the JWT and sends it to the user. When the user makes API calls to the application, the user passes the JWT along with the API call. In this setup, the application server would be configured to verify that the incoming JWT are created by the authentication server (the verification process will be explained in more detail later). So, when the user makes API calls with the attached JWT, the application can use the JWT to verify that the API call is coming from an authenticated user.
Now, the JWT itself, and how it’s constructed and verified, will be examined in more depth.
Step 1. Create the HEADER
The header component of the JWT contains information about how the JWT signature should be computed. The header is a JSON object in the following format:
In this JSON, the value of the “typ” key specifies that the object is a JWT, and the value of the “alg” key specifies which hashing algorithm is being used to create the JWT signature component. In our example, we’re using the HMAC-SHA256 algorithm, a hashing algorithm that uses a secret key, to compute the signature (discussed in more detail in step 3).
Step 2. Create the PAYLOAD
The payload component of the JWT is the data that‘s stored inside the JWT (this data is also referred to as the “claims” of the JWT). In our example, the authentication server creates a JWT with the user information stored inside of it, specifically the user ID.
The data inside the payload is referred to as the “claims” of the token.In our example, we are only putting one claim into the payload. You can put as many claims as you like. There are several different standard claims for the JWT payload, such as “iss” the issuer, “sub” the subject, and “exp” the expiration time. These fields can be useful when creating JWT, but they are optional. See the wikipedia page on JWT for a more detailed list of JWT standard fields.
Keep in mind that the size of the data will affect the overall size of the JWT, this generally isn’t an issue but having excessively large JWT may negatively affect performance and cause latency.
Step 3. Create the SIGNATURE
The signature is computed using the following pseudo code:
// signature algorithmdata = base64urlEncode( header ) + “.” + base64urlEncode( payload )signature = Hash( data, secret );What this algorithm does is base64url encodes the header and the payload created in steps 1 and 2. The algorithm then joins the resulting encoded strings together with a period (.) in between them. In our pseudo code, this joined string is assigned to data. To get the JWT signature, the data string is hashed with the secret key using the hashing algorithm specified in the JWT header.
In our example, both the header, and the payload are base64url encoded as:
// header eyJ0eXAiOiJKV1QiLCJhbGciOiJIUzI1NiJ9// payload eyJ1c2VySWQiOiJiMDhmODZhZi0zNWRhLTQ4ZjItOGZhYi1jZWYzOTA0NjYwYmQifQThen, using the joined encoded header and payload, and applying the specified signature algorithm(HS256) on the data string with the secret key set as the string “secret”, we get the following JWT Signature:
// signature-xN_h82PHVTCMA9vdoHrcZxH-x5mb11y1537t3rGzcMStep 4. Put All Three JWT Components Together
Now that we have created all three components, we can create the JWT. Remembering the header.payload.signature structure of the JWT, we simply need to combine the components, with periods (.) separating them. We use the base64url encoded versions of the header and of the payload, and the signature we arrived at in step 3.
// JWT Token eyJ0eXAiOiJKV1QiLCJhbGciOiJIUzI1NiJ9.eyJ1c2VySWQiOiJiMDhmODZhZi0zNWRhLTQ4ZjItOGZhYi1jZWYzOTA0NjYwYmQifQ.-xN_h82PHVTCMA9vdoHrcZxH-x5mb11y1537t3rGzcMYou can try creating your own JWT through your browser at jwt.io.
Going back to our example, the authentication server can now send this JWT to the user.
How does JWT protect our data?
It is important to understand that the purpose of using JWT is NOT to hide or obscure data in any way. The reason why JWT are used is to prove that the sent data was actually created by an authentic source.
As demonstrated in the previous steps, the data inside a JWT is encoded and signed, not encrypted. The purpose of encoding data is to transform the data’s structure. Signing data allows the data receiver to verify the authenticity of the source of the data. So encoding and signing data does NOT secure the data. On the other hand, the main purpose of encryption is to secure the data and to prevent unauthorized access. For a more detailed explanation of the differences between encoding and encryption, and also for more information on how hashing works, see this article.
Since JWT are signed and encoded only, and since JWT are not encrypted, JWT do not guarantee any security for sensitive data.Step 5. Verifying the JWT
In our simple 3 entity example, we are using a JWT that is signed by the HS256 algorithm where only the authentication server and the application server know the secret key. The application server receives the secret key from the authentication server when the application sets up its authentication process. Since the application knows the secret key, when the user makes a JWT-attached API call to the application, the application can perform the same signature algorithm as in Step 3 on the JWT. The application can then verify that the signature obtained from it’s own hashing operation matches the signature on the JWT itself (i.e. it matches the JWT signature created by the authentication server). If the signatures match, then that means the JWT is valid which indicates that the API call is coming from an authentic source. Otherwise, if the signatures don’t match, then it means that the received JWT is invalid, which may be an indicator of a potential attack on the application. So by verifying the JWT, the application adds a layer of trust between itself and the user.
In Conclusion
We went over what JWT are, how they are created and validated, and how they can be used to ensure trust between an application and its users. This is a starting point for understanding the fundamentals of JWT and why they are useful. JWT are just one piece of the puzzle in ensuring trust and security in your application.
It should be noted that the JWT authentication setup described in this article is using a symmetric key algorithm (HS256). You can also set up your JWT authentication in a similar way except using an asymmetric algorithm (such as RS256) where the authentication server has a secret key, and the application server has a public key. Check out this Stack Overflow question for a detailed breakdown of the differences between using symmetric and asymmetric algorithms.
It should also be noted that JWT should be sent over HTTPS connections (not HTTP). Having HTTPS helps prevents unauthorized users from stealing the sent JWT by making it so that the communication between the servers and the user cannot be intercepted . Also having an expiration in your JWT payload, a short one in particular, is important so that if old JWT ever get compromised, they will be considered invalid and can no longer be used.
If you enjoyed this article and are writing handlers for AWS Lambda and are implementing JWT, please check out our project: Vandium

## Slide 83: JWT
Boarding Configuration
Acquiring an Access Token
Create Data Point Mapping
Exchange Data
DataSource Configuration
Provisioning an Agent
Onboarding the Agent
Notes: https://stackoverflow.com/questions/4657416/difference-between-encoding-and-encryption
https://medium.com/vandium-software/5-easy-steps-to-understanding-json-web-tokens-jwt-1164c0adfcec
In this example, the user first signs into the authentication server using the authentication server’s login system (e.g. username and password, Facebook login, Google login, etc). The authentication server then creates the JWT and sends it to the user. When the user makes API calls to the application, the user passes the JWT along with the API call. In this setup, the application server would be configured to verify that the incoming JWT are created by the authentication server (the verification process will be explained in more detail later). So, when the user makes API calls with the attached JWT, the application can use the JWT to verify that the API call is coming from an authenticated user.
Now, the JWT itself, and how it’s constructed and verified, will be examined in more depth.
Step 1. Create the HEADER
The header component of the JWT contains information about how the JWT signature should be computed. The header is a JSON object in the following format:
In this JSON, the value of the “typ” key specifies that the object is a JWT, and the value of the “alg” key specifies which hashing algorithm is being used to create the JWT signature component. In our example, we’re using the HMAC-SHA256 algorithm, a hashing algorithm that uses a secret key, to compute the signature (discussed in more detail in step 3).
Step 2. Create the PAYLOAD
The payload component of the JWT is the data that‘s stored inside the JWT (this data is also referred to as the “claims” of the JWT). In our example, the authentication server creates a JWT with the user information stored inside of it, specifically the user ID.
The data inside the payload is referred to as the “claims” of the token.In our example, we are only putting one claim into the payload. You can put as many claims as you like. There are several different standard claims for the JWT payload, such as “iss” the issuer, “sub” the subject, and “exp” the expiration time. These fields can be useful when creating JWT, but they are optional. See the wikipedia page on JWT for a more detailed list of JWT standard fields.
Keep in mind that the size of the data will affect the overall size of the JWT, this generally isn’t an issue but having excessively large JWT may negatively affect performance and cause latency.
Step 3. Create the SIGNATURE
The signature is computed using the following pseudo code:
// signature algorithmdata = base64urlEncode( header ) + “.” + base64urlEncode( payload )signature = Hash( data, secret );What this algorithm does is base64url encodes the header and the payload created in steps 1 and 2. The algorithm then joins the resulting encoded strings together with a period (.) in between them. In our pseudo code, this joined string is assigned to data. To get the JWT signature, the data string is hashed with the secret key using the hashing algorithm specified in the JWT header.
In our example, both the header, and the payload are base64url encoded as:
// header eyJ0eXAiOiJKV1QiLCJhbGciOiJIUzI1NiJ9// payload eyJ1c2VySWQiOiJiMDhmODZhZi0zNWRhLTQ4ZjItOGZhYi1jZWYzOTA0NjYwYmQifQThen, using the joined encoded header and payload, and applying the specified signature algorithm(HS256) on the data string with the secret key set as the string “secret”, we get the following JWT Signature:
// signature-xN_h82PHVTCMA9vdoHrcZxH-x5mb11y1537t3rGzcMStep 4. Put All Three JWT Components Together
Now that we have created all three components, we can create the JWT. Remembering the header.payload.signature structure of the JWT, we simply need to combine the components, with periods (.) separating them. We use the base64url encoded versions of the header and of the payload, and the signature we arrived at in step 3.
// JWT Token eyJ0eXAiOiJKV1QiLCJhbGciOiJIUzI1NiJ9.eyJ1c2VySWQiOiJiMDhmODZhZi0zNWRhLTQ4ZjItOGZhYi1jZWYzOTA0NjYwYmQifQ.-xN_h82PHVTCMA9vdoHrcZxH-x5mb11y1537t3rGzcMYou can try creating your own JWT through your browser at jwt.io.
Going back to our example, the authentication server can now send this JWT to the user.
How does JWT protect our data?
It is important to understand that the purpose of using JWT is NOT to hide or obscure data in any way. The reason why JWT are used is to prove that the sent data was actually created by an authentic source.
As demonstrated in the previous steps, the data inside a JWT is encoded and signed, not encrypted. The purpose of encoding data is to transform the data’s structure. Signing data allows the data receiver to verify the authenticity of the source of the data. So encoding and signing data does NOT secure the data. On the other hand, the main purpose of encryption is to secure the data and to prevent unauthorized access. For a more detailed explanation of the differences between encoding and encryption, and also for more information on how hashing works, see this article.
Since JWT are signed and encoded only, and since JWT are not encrypted, JWT do not guarantee any security for sensitive data.Step 5. Verifying the JWT
In our simple 3 entity example, we are using a JWT that is signed by the HS256 algorithm where only the authentication server and the application server know the secret key. The application server receives the secret key from the authentication server when the application sets up its authentication process. Since the application knows the secret key, when the user makes a JWT-attached API call to the application, the application can perform the same signature algorithm as in Step 3 on the JWT. The application can then verify that the signature obtained from it’s own hashing operation matches the signature on the JWT itself (i.e. it matches the JWT signature created by the authentication server). If the signatures match, then that means the JWT is valid which indicates that the API call is coming from an authentic source. Otherwise, if the signatures don’t match, then it means that the received JWT is invalid, which may be an indicator of a potential attack on the application. So by verifying the JWT, the application adds a layer of trust between itself and the user.
In Conclusion
We went over what JWT are, how they are created and validated, and how they can be used to ensure trust between an application and its users. This is a starting point for understanding the fundamentals of JWT and why they are useful. JWT are just one piece of the puzzle in ensuring trust and security in your application.
It should be noted that the JWT authentication setup described in this article is using a symmetric key algorithm (HS256). You can also set up your JWT authentication in a similar way except using an asymmetric algorithm (such as RS256) where the authentication server has a secret key, and the application server has a public key. Check out this Stack Overflow question for a detailed breakdown of the differences between using symmetric and asymmetric algorithms.
It should also be noted that JWT should be sent over HTTPS connections (not HTTP). Having HTTPS helps prevents unauthorized users from stealing the sent JWT by making it so that the communication between the servers and the user cannot be intercepted . Also having an expiration in your JWT payload, a short one in particular, is important so that if old JWT ever get compromised, they will be considered invalid and can no longer be used.
If you enjoyed this article and are writing handlers for AWS Lambda and are implementing JWT, please check out our project: Vandium

## Slide 84: MindConnect API Onboarding Agent
Onboarding the Agent
Acquiring an Access Token
Create Data Point Mapping
Exchange Data
DataSource Configuration
Provisioning an Agent
Boarding Configuration
After acquiring the IAT ( Initial access token ), Agent needs to register with MindSphere. This registration process takes place in accordance with the OAuth 2.0 Authorization protocol.
Agent sends an HTTP POST request to the MindSphere, The way request constructed varies slightly depending on the Agent Security Profile.
Initial contact (Onboarding) We need to ensure that agents, that connect the first time to the MindSphere, become a valid communication partner having a known human owner.
Regular interaction Once an agent has become a known and authorized entity in MindSphere, we need to ensure that each time it reconnects, we are still talking to the same agent.

## Slide 85: MindConnect API Agent with SHARED_SECRET security profile Registration
Agent sends an HTTP POST request with an empty body, MindSphere receives the request, validates it (IAT validation, mandatory headers validation etc) and if validation succeeds, creates an Agent SHARED_SECRET and stores it in its database with a predefined SHARED_SECRET expiration time (7 days by default). MindSphere creates another token called Registration Access Token (RAT) for the client. When the client_secret expiration occurs client is expected to sent another Registration Update Request (Key Rotation) RAT token instead of IAT so the registration can be renewed.
POST /api/agentmanagement/v3/register
Onboarding the Agent
Acquiring an Access Token
Create Data Point Mapping
Exchange Data
DataSource Configuration
Provisioning an Agent
Boarding Configuration
POST /api/agentmanagement/v3/register HTTP/1.1
Content-Type: application/json
Accept: application/json
Authorization: Bearer
eyJhbGciOiJSUzI1NiIsInR5cCI6IkpXVCJ9.eyJpc3MiOiJTQ0kiLCJzdWIiOiJ0 ZXN0LWFnZW50IiwiYXVkIjpbIkFJQU0iXSwiaWF0Ijox…
… //Initial Access Token (IAT) acquired
==
Host: southgate.<region-env>.mindsphere.io
{} //empty JSON Object
Notes: S7comm (S7 Communication) is a Siemens proprietary protocol that runs between programmable logic controllers (PLCs) of the Siemens S7-300/400 family.
It is used for PLC programming, exchanging data between PLCs, accessing PLC data from SCADA (supervisory control and data acquisition) systems and diagnostic purposes

## Slide 86: MindConnect API Register Response With SHARED_SECRET security Profile
Onboarding the Agent
Acquiring an Access Token
Create Data Point Mapping
Exchange Data
DataSource Configuration
Provisioning an Agent
Boarding Configuration
HTTP/1.1 201 Created
Content-Type: application/json
Cache-Control: no-store
Pragma: no-cache
{
"client_id": "008ceaf9dff443ee94205f903aa545c4",
"token_endpoint_auth_method": "client_secret_jwt",
"grant_types": [
"client_credentials"
],
"client_secret": "ly7zmXbz0Izla6B82xlAYRVBcKDcCFatwmnHQmR8Ycw",
"client_secret_expires_at": 1514206768,
"registration_access_token": "eyJraWQiOiJrZXktaWQtMSI......",
"registration_client_uri": "https://southgate.eu-central-rc.mindsphere.io/api/agentmanagement/v3/regi
ster/008ceaf9dff443ee94205f903aa545c4"
}
Notes: S7comm (S7 Communication) is a Siemens proprietary protocol that runs between programmable logic controllers (PLCs) of the Siemens S7-300/400 family.
It is used for PLC programming, exchanging data between PLCs, accessing PLC data from SCADA (supervisory control and data acquisition) systems and diagnostic purposes

## Slide 87: MindConnect API Register Response With SHARED_SECRET security Profile
Onboarding the Agent
Acquiring an Access Token
Create Data Point Mapping
Exchange Data
DataSource Configuration
Provisioning an Agent
Boarding Configuration
Parameter | Description | Remarks
client_id | Holds agent id | 
token_endpoint_auth_method |  | 
grant_types | Agents security profile, set during provisioning step. | 
client_secret | Generated Client Secret, Client will use when requesting access token | 
client_secret_expires_at | Time generated client secret will expire | Client needs to re-register with RAT if expiration occurs. Default value is 7 days
registration_access_token | Registration Access Token, client needs this token to renew its registration | 
registration_client_uri | URI to use when client renews its registration | 
Notes: S7comm (S7 Communication) is a Siemens proprietary protocol that runs between programmable logic controllers (PLCs) of the Siemens S7-300/400 family.
It is used for PLC programming, exchanging data between PLCs, accessing PLC data from SCADA (supervisory control and data acquisition) systems and diagnostic purposes

## Slide 88: MindConnect API Refreshing a Registration
By default, each registered agent (either RSA 3072 or Shared Secret security profile) has its credentials valid for 7 days. After this period MindSphere will not grant access tokens to the agent and it will render the agent credentials invalid. The agent needs to re-register (Key-Rotation) to MindSphere providing its Registration Access Token (RAT). The agent needs to perform this request to the URL value of registration_client_uri. This URL is provided in the JSON body of the HTTP response 201 Created to a successful registration.
PUT /api/agentmanagement/v3/register/{agent_id}
Onboarding the Agent
Acquiring an Access Token
Create Data Point Mapping
Exchange Data
DataSource Configuration
Provisioning an Agent
Boarding Configuration
PUT /api/agentmanagement/v3/register/{agent_id} HTTP/1.1
Content-Type: application/json
Accept: application/json
Authorization: Bearer
eyJhbGciOiJSUzI1NiIsInR5cCI6IkpXVCJ9.eyJpc3MiOiJTQ0kiLCJzdWIiOiJ0 ZXN0LWFnZW50IiwiYXVkIjpbIkFJQU0iXSwiaWF0Ijox…
… //Registration Access Token (RAT)
Host: authorizationserver.mindsphere.com
{
"client_id": "agentid"
}
Notes: S7comm (S7 Communication) is a Siemens proprietary protocol that runs between programmable logic controllers (PLCs) of the Siemens S7-300/400 family.
It is used for PLC programming, exchanging data between PLCs, accessing PLC data from SCADA (supervisory control and data acquisition) systems and diagnostic purposes

## Slide 89: MindConnect API Refreshing a Registration
If the RAT is correct and the provided client Id matches, a new registration access token is returned to the client. The old registration access token must be discarded by the client, MindSphere discards the old RAT automatically.
MindSphere returns an HTTP response 200 OK. The structure of the JSON body is the same as for the initial registration of the agent:
Onboarding the Agent
Acquiring an Access Token
Create Data Point Mapping
Exchange Data
DataSource Configuration
Provisioning an Agent
Boarding Configuration
{
"client_id": "f03714282d374383abff1cfd486d231c",
"token_endpoint_auth_method": "client_secret_jwt",
"grant_types": [
"client_credentials"
],
"client_secret": "OsROMak-0iGEt_P7hr-Dd_Vl6PzP4M6n9r8ssX2YF4M",
"client_secret_expires_at": 1526996947,
"registration_access_token": "eyJraWQiOiJrZXktaWQtMSIsInR5cCI6IkpXVCIsImFsZyI6IlJTMjU2I……",
"registration_client_uri": "https://southgate.eu1.mindsphere.io/api/agentmanagement/v3/register/f03714282d374383abff1cfd486d231c"
}
Notes: S7comm (S7 Communication) is a Siemens proprietary protocol that runs between programmable logic controllers (PLCs) of the Siemens S7-300/400 family.
It is used for PLC programming, exchanging data between PLCs, accessing PLC data from SCADA (supervisory control and data acquisition) systems and diagnostic purposes

## Slide 90: MindConnect API Demonstration
Onboarding the Agent
Key rotation
Onboarding the Agent
Acquiring an Access Token
Create Data Point Mapping
Exchange Data
DataSource Configuration
Provisioning an Agent
Boarding Configuration

## Slide 91: MindConnect API Hands-On Exercise 4: Onboarding the Agent
Hands-on
Task 1: Onboarding the agent
Task 2: Key rotation
Onboarding the Agent
Acquiring an Access Token
Create Data Point Mapping
Exchange Data
DataSource Configuration
Provisioning an Agent
Boarding Configuration

## Slide 92: MindConnect API Acquiring an agent access token
Acquiring an Access Token
Onboarding the Agent
Create Data Point Mapping
Exchange Data
DataSource Configuration
Provisioning an Agent
Boarding Configuration
Each onboarded agent is required to get an access token in order to use any services offered by MindSphere. MindSphere grants access tokens to clients for which token generation and grants comply with the rules of the OAuth 2.0 authorization framework.
MindSphere receives token requests (HTTP POST) from clients and grants access tokens back to them (HTTP 200 OK). Before granting an access token, the Access Token service performs the following checks:
The token request contains mandatory and expected headers.
The client is a known client (exists in the database).
The client status is ONBOARDED.

## Slide 93: MindConnect API Acquiring an agent access token
Granting of access tokens is provided by the token endpoint of the Agent Management Service. This is a sample client access token request expected by MindSphere:
POST /api/agentmanagement/v3/oauth/token HTTP/1.1
Content-Type: application/x-www-form-urlencoded
Host: localhost: 8061
content-length: 510
Connection: keep-alive
grant_type=client_credentials&client_assertion_type=urn:ietf:params:oauth:client-assertion-type:jwt-bearer&client_assertion=eyJhbGciOiJSUzI1NiIsInR5cCI6IkpXVCJ9……
Acquiring an Access Token
Onboarding the Agent
Create Data Point Mapping
Exchange Data
DataSource Configuration
Provisioning an Agent
Boarding Configuration
Notes: S7comm (S7 Communication) is a Siemens proprietary protocol that runs between programmable logic controllers (PLCs) of the Siemens S7-300/400 family.
It is used for PLC programming, exchanging data between PLCs, accessing PLC data from SCADA (supervisory control and data acquisition) systems and diagnostic purposes

## Slide 94: MindConnect API Acquiring an agent access token
grant_type=client_credentials&client_assertion_type=urn:ietf:params:oauth:client-assertion-type:jwt-bearer&client_assertion=eyJhbGciOiJSUzI1NiIsInR5cCI6IkpXVCJ9……
Acquiring an Access Token
Onboarding the Agent
Create Data Point Mapping
Exchange Data
DataSource Configuration
Provisioning an Agent
Boarding Configuration
Parameter | Description | Remarks
grant_type | Defines the OAuth 2.0 access token flow requested by the client. MindSphere supports only client_credentials. | 
client_assertion_type | Defines the assertion type (assertion is defined in RFC 7521). MindSphere supports only the jwt-bearer type assertion urn:ietf:params:oauth:client-assertion-type:jwt-bearer (for details see RFC 7523, Section 2.2 "Using JWTs for Client Authentication"). | 
client_assertion | Contains the assertion (self-signed JWT) signed (by the client) with client secret or client public key depending on the client security profile. | 
Notes: S7comm (S7 Communication) is a Siemens proprietary protocol that runs between programmable logic controllers (PLCs) of the Siemens S7-300/400 family.
It is used for PLC programming, exchanging data between PLCs, accessing PLC data from SCADA (supervisory control and data acquisition) systems and diagnostic purposes

## Slide 95: MindConnect API Signed JWT
Client requests contain a self-signed JWT, conveyed with the body parameter client_assertion. This client assertion is required to be signed with the credential data provided at the registration:
{
"alg": "HS256",
"typ": "JWT"
}
{
"iss": "f03714282d374383abff1cfd486d231c", //client_id
"sub": "f03714282d374383abff1cfd486d231c", //client_id
"aud": [
"southgate"
],
"iat": 1526393304, // date.getTime()
"nbf": 1526393304,
"exp": 1526998104,
"jti": "826d75fa-4f16-4aaa-ad85-807b8a61957b", //unique id
"schemas": [
"urn:siemens:mindsphere:v1"
],
"ten": „academy2"
}
Acquiring an Access Token
Onboarding the Agent
Create Data Point Mapping
Exchange Data
DataSource Configuration
Provisioning an Agent
Boarding Configuration
Notes: S7comm (S7 Communication) is a Siemens proprietary protocol that runs between programmable logic controllers (PLCs) of the Siemens S7-300/400 family.
It is used for PLC programming, exchanging data between PLCs, accessing PLC data from SCADA (supervisory control and data acquisition) systems and diagnostic purposes

## Slide 96: MindConnect API Acquiring an agent access token
When all tests have been successfully passed, MindSphere returns an HTTP response 200 OK that holds an access token. The returned access token is actually a signed JWT, which is valid for 1 hour by default
{
"access_token": "eyJraWQiOiJrZXktaWQtMSIsImF……zgw",
"token_type": "Bearer",
"expires_in": 3600,
"scope": [
"mdsp:core:DefaultAgent"
],
"jti": "0d0f345f-b036-4484-851a-deced2022144"
}
Acquiring an Access Token
Onboarding the Agent
Create Data Point Mapping
Exchange Data
DataSource Configuration
Provisioning an Agent
Boarding Configuration
Notes: S7comm (S7 Communication) is a Siemens proprietary protocol that runs between programmable logic controllers (PLCs) of the Siemens S7-300/400 family.
It is used for PLC programming, exchanging data between PLCs, accessing PLC data from SCADA (supervisory control and data acquisition) systems and diagnostic purposes

## Slide 97: MindConnect API Demonstration
Create and sign the JWT
Acquire Access Token
Onboarding the Agent
Create Data Point Mapping
Exchange Data
DataSource Configuration
Provisioning an Agent
Boarding Configuration
Acquiring an Access Token

## Slide 98: MindConnect API Hands-On Exercise 5: Acquire Access Token
Hands-on
Task 1: Create and sign the JWT
Task 2: Acquire Access Token
Onboarding the Agent
Create Data Point Mapping
Exchange Data
DataSource Configuration
Provisioning an Agent
Boarding Configuration
Acquiring an Access Token

## Slide 99: MindConnect API Data Source and Data Points
DataSource Configuration
Onboarding the Agent
Create Data Point Mapping
Exchange Data
Acquiring an Access Token
Provisioning an Agent
Boarding Configuration
If Agent needs to upload data to MindSphere, MindSphere needs additional configuration to know how to interpret agents data streams. This configuration requires 3 definitions within MindSphere.
  Data Source Provisioning
  Property Set (Data Points) Provisioning
  Creating a Mapping for Property Set and Data Source
"Data Source" is a logical group that holds so called "Data Points". Data points hold meta data about a specific metric that the Agent generates or measures. An example is: "if an agent measures ambient temperature and pressure data. Each of this two measurement needs to be defined as separate "Data Points".

## Slide 100: MindConnect API Create Data Source Configuration
DataSource Configuration
Onboarding the Agent
Create Data Point Mapping
Exchange Data
Acquiring an Access Token
Provisioning an Agent
Boarding Configuration
Mindsphere provides dataSourceConfiguration endpoint to create DataPoints and the DataSource they are grouped into.
PUT /api/agentmanagement/v3/agents/{id}/dataSourceConfiguration
HTTP/1.1 PUT api/agentmanagement/v3/agents/{id}/dataSourceConfiguration
Content-Type: application/json
If-Match: etag
Authorization: Bearer eyx...
{
"configurationId": "string",
"dataSources": [
{
"name": "string",
"description": "string",
"dataPoints": [
{
"id": "string",
"name": "string",
"description": "string",
"type": "int",
"unit": "string",
"customData": {}
}
],
"customData": {}
}
]
}

## Slide 101: MindConnect API Data Source Configuration Response
DataSource Configuration
Onboarding the Agent
Create Data Point Mapping
Exchange Data
Acquiring an Access Token
Provisioning an Agent
Boarding Configuration
If successful, MindSphere will respond with HTTP 200 OK with JSON body that holds the created DataSource Configuration. "configurationId" must be taken note since, during consuming exchange services this parameter needs to be provided back to MindSphere.
{
"id": "string",
"eTag": "2",
"configurationId": "string",
"dataSources": [
{
"name": "string",
"description": "string",
"dataPoints": [
{
"id": "string",
"name": "string",
"description": "string",
"type": "int",
"unit": "string",
"customData": {}
}
],
"customData": {}
…

## Slide 102: MindConnect API Demonstration
Configure and upload Data Source
DataSource Configuration
Onboarding the Agent
Create Data Point Mapping
Exchange Data
Acquiring an Access Token
Provisioning an Agent
Boarding Configuration

## Slide 103: MindConnect API Hands-On Exercise: Configure and Upload Data Source
Hands-on
Task 1: Configure and upload Data Source
DataSource Configuration
Onboarding the Agent
Create Data Point Mapping
Exchange Data
Acquiring an Access Token
Provisioning an Agent
Boarding Configuration

## Slide 104: MindConnect API
Create Data Point Mapping
Onboarding the Agent
DataSource Configuration
Exchange Data
Acquiring an Access Token
Provisioning an Agent
Boarding Configuration
At this step we have a Data Source (Grouping Object for the Data Points) and a Property Set (Grouping object for the Properties) already defined in the system, a Mapping needs to be defined so that MindSphere can interpret data flowing through agent to MindSphere. Data Source configuration holds meta data about Agent side where as Property Set holds Meta data about IOT side. MindSphere needs additional configuration to map from Data Point meta to Property meta, This information is called a mapping. This mapping is done one by one, for each data point to property. In other words, we need to map Data Points to Properties.
In order to create a mapping dataPointMappings
Endpoint: (<<_gateway_url>>/api/mindconnect/v3/dataPointMappings)
HTTP/1.1 POST
Content-Type: Application/Json
Authorization: Bearer eyc..
{
"agentId": "11961bc396cd4a87a9b26b723f5b7ba0",
"dataPointId": "DP0001",
"entityId": "83e78008eadf453bae4f5c7bef3db550",
"propertySetName": "ElectricalProperties",
"propertyName": "Voltage"
}

## Slide 105: MindConnect API
Create Data Point Mapping
Onboarding the Agent
DataSource Configuration
Exchange Data
Acquiring an Access Token
Provisioning an Agent
Boarding Configuration
In order to create a mapping dataPointMappings
Endpoint: (<<_gateway_url>>/api/mindconnect/v3/dataPointMappings)
Parameter | Description | Remarks
agentId | Unique agent id | 
dataPointId | DataSource Configurations Data Point Id | 
entityId | Entities Id, this Agent created from | 
propertySetName | Property Set name created for this Agent. (Entity EntityType PropertySet) | Client needs to re-register with RAT if expiration occurs. Default value is 7 days
propertyName | Related property name within the property set we are binding to data point | 

## Slide 106: MindConnect API
Create Data Point Mapping
Onboarding the Agent
DataSource Configuration
Exchange Data
Acquiring an Access Token
Provisioning an Agent
Boarding Configuration
If successful, MindConnect responds with 201 Created with JSON body that holds created mapping configuration. This step only maps one data point to one property if more mapping is needed this step must be repeated.
{
"id": "4fad6258-5def-4d84-a4c2-1481b209c116",
"agentId": "11961bc396cd4a87a9b26b723f5b7ba0",
"dataPointId": "DP0001",
"dataPointUnit": "%",
"dataPointType": "INT",
"entityId": "83e78008eadf453bae4f5c7bef3db550",
"propertySetName": "ElectricalProperties",
"propertyName": "Voltage",
"propertyUnit": "%",
"propertyType": "INT",
"qualityEnabled": true
}

## Slide 107: MindConnect API Exchange Data
Exchange Data
Onboarding the Agent
DataSource Configuration
Create Data Point Mapping
Acquiring an Access Token
Provisioning an Agent
Boarding Configuration
The MindSphere exchange endpoint of the MindConnect API provides the agent with the capability of uploading its data to MindSphere. This data can be of type:
Time Series
File Upload
The format conforms to a subset of the HTTP multipart specification, but only permits nesting of 2 levels. Below is a sample exchange message content:
--f0Ve5iPP2ySppIcDSR6Bak
Content-Type: multipart/related;boundary=penFL6sBQHJJUN3HA4ftqC
--penFL6sBQHJJUN3HA4ftqC
Content-Type: application/vnd.siemens.mindsphere.meta+json
{
"type": "item",
"version": "1.0",
"payload": {
"type": "standardTimeSeries",
"version": "1.0",
"details": {
"configurationId": "{{_configuration_id}}"
}
}
}
--initial boundary
--boundary1
Metadata
--boundary1
Payload
--boundary1–-
--initial boundary--
multipart messages

## Slide 108: MindConnect API Workflow details
Exchange Data
Onboarding the Agent
DataSource Configuration
Create Data Point Mapping
Acquiring an Access Token
Provisioning an Agent
Boarding Configuration
--penFL6sBQHJJUN3HA4ftqC
Content-Type: application/json
[
{
"timestamp": "2017-02-01T08:30:03.780Z",
"values": [
{
"dataPointId": "{{_datapoint_id_1}}",
"value": "9856",
"qualityCode": "0"
},
{
"dataPointId": "{{_datapoint_id_2}}",
"value": "3766",
"qualityCode": "0"
}
]
}
]
--penFL6sBQHJJUN3HA4ftqC--
--f0Ve5iPP2ySppIcDSR6Bak--
--initial boundary
--boundary1
Metadata
--boundary1
Payload
--boundary1–
--initial boundary--
multipart messages

## Slide 109: MindConnect API Workflow details
Exchange Data
Onboarding the Agent
DataSource Configuration
Create Data Point Mapping
Acquiring an Access Token
Provisioning an Agent
Boarding Configuration
The MindSphere exchange endpoint of the MindConnect API provides the agent with the capability of uploading its data to MindSphere. This data can be of type:
Time Series
File Upload
The format conforms to a subset of the HTTP multipart specification, but only permits nesting of 2 levels. Below is a sample exchange message content:
--f0Ve5iPP2ySppIcDSR6Bak
Content-Type: multipart/related;boundary=penFL6sBQHJJUN3HA4ftqC
--penFL6sBQHJJUN3HA4ftqC
Content-Type: application/vnd.siemens.mindsphere.meta+json
{
"type": "item",
"version": "1.0",
"payload": {
"type": "standardTimeSeries",
"version": "1.0",
"details": {
"configurationId": "{{_configuration_id}}"
}
}
}

## Slide 110: MindConnect API Demonstration: Exchange Data
Exchange Data
Onboarding the Agent
DataSource Configuration
Create Data Point Mapping
Acquiring an Access Token
Provisioning an Agent
Boarding Configuration
Create data mapping
Prepare the time series to be uploaded
Exchange Data

## Slide 111: MindConnect API Hands-On Exercise 7: Exchange Data
Hands-on
Task 1: Create data mapping
Task 2: Prepare the time series to be uploaded
Task 3: Exchange Data
Exchange Data
Onboarding the Agent
DataSource Configuration
Create Data Point Mapping
Acquiring an Access Token
Provisioning an Agent
Boarding Configuration

## Slide 112
MindSphere
Cloud Foundry Essentials

## Slide 113: Cloud Foundry Essentials Learning Goals
Cloud Foundry
Cloud Foundry Foundation
Build packs
What is Cloud Foundry
&
what is its advantage?

## Slide 114: Cloud Foundry General
Multi cloud application platform as a service (PaaS)
SpringSource, VMWare, EMC, Pivotal
Development started in 2009
First version in 2012
Onsi Fakhouri, VP Cloud R&D, Pivotal

## Slide 115: Cloud Foundry Cloud Foundry Foundation
Cloud Foundry Foundation is a 501(c)(6) nonprofit, open source project.
"Our purpose is to make Cloud Foundry the leading application platform for cloud computing worldwide."
Members (extract):
Cisco
IBM
Pivotal
SAP
SUSE
VMware

## Slide 116: Cloud Foundry Overview
Clients
CLI
Build packs
My Services
Backing services
my-pub-cloud-service.io
deploy
Config File manifest.yml
PHP
Go
Python
Java
Node.js
Ruby
.net core
Static file
App
Notes: MindSphere uses 2.9.x runtime with hardened stemcells
Buildpacks Java, Node.js, .NET Core and staticfile

## Slide 117: Cloud Foundry Org-Space concept
Third Party 1 Org
App Space 1
Backing Services Third Party 1 Space 1
Internet https
Customer
Third Party 1 App 1
Third Party 1 UI/Application 1
Third Party 1 App 2
App Space 2
Third Party 1 App 3
Third Party 1 App 4
Third Party 1 UI/Application 2
Backing Services
Third Party 1 Space 2
Third Party 2 Org
App Space 1
Third Party 2 App 1
Backing Services
Third Party 2 Space 1
Third Party 2 UI/Application 1

## Slide 118: Cloud Foundry Security by MindSphere
Industrially hardened Stemcells
Managed Buildpacks with a high level of security standard (e.g. CVE scanning)
Managed Backing Services with automated backup capabilities (plan medium or higher)
Separation of Concerns - clear separation of development and production environments)
Positive Security Concept for Applications and APIs

## Slide 119: Cloud Foundry manifest.yml

## Slide 120: Cloud Foundry Demo
Login to CloudFoundry
Show Proxy-Settings
Demo CloudFoundry CLI command

## Slide 121: Cloud Foundry
Exercise
Step-by-step Login

## Slide 122: Cloud Foundry Exercise: Step-by-step Login
Install CloudFoundry CLI (if not already prepared)
Optional: Set proxy configuration in CMD or bash
Define endpoint: cf api https://api.cf.eu1.mindsphere.io
Login using the command: cf login -sso
Visit https://login.cf.eu1.mindsphere.io/passcode to get an One Time Code
Login using the WebKey Login Form
Type in your MindSphere Credentials
Copy the One Time Code and use in the CF CLI
Select your assigned Cloud Foundry ORG (if asked)
Select a Cloud Foundry Space (if asked)

## Slide 123: Cloud Foundry Essentials Summary
What is Cloud Foundry?
Cloud Foundry is the leading application platform for cloud computing worldwide.
What is its advantage?
With CloudFoundry you have an easy way to run your application inside MindSphere

## Slide 124
MindSphere
Hello world app

## Slide 125: Hello world app Learning Goals
LaunchPad presentation
Overall concept of what we need to do
Demo and exercise
Concept of developing and pushing "Hello World" app

## Slide 126: What do we want to do?

## Slide 127: What do we have to do?
Developer
helloWorld
hw
CloudFoundry
Space: dev
App
hw
Org: academy2
Tenant
LaunchPad
App
hw
academy2
cf push
1
register
2

## Slide 128: Demo: Push and register an application

## Slide 129: Hello World app
Create and register a hello world app
Exercise

## Slide 130: Exercise: Create and register a hello world app
Create application
  Goto folder 010-helloworld
  Create a static html file that shows "Hello World"
  Check manifest.yml
  Choose the correct buildpack
Push this application
  Enter: cf push
Register
  Go to Developer Cockpit
  Create new application
  Enter: Name, Display name, Version and App Icon
  Create a component
    Component name: app name from manifest.yml
    Cloud Foundry Direct URL: cf a
    Add endpoint ("/**") with + button
  Click Save
Add application scope
  Goto Authorization Management / App roles
  Search for you app
  Click on "Create scope"
  Add a scope name
  Activate both "ADMIN" and "USER" checkboxes
  Click "Save"
Register application
  Go back to the Dashboard in Developer Cockpit
  Choose your application
  Click on Register
Add application scope to your user
  Goto MindSphere Launchpad
  Open Settings app
  At users, search for your user
  Click "Edit direct assignments"
  Search for your app under "Filter"
  Select admin and user role and confirm

## Slide 131: Hello world app Summary
What do we need to do in order to register an application?
The application has to be pushed to CloudFoundry at first and can then be registered.

## Slide 132
MindSphere
Asset Management Service (Part I)

## Slide 133: MindSphere API - Asset Management Service Learning Goals
Asset concept
Requests to use
How do we read information of the asset &
how can we navigate through the asset hierarchy?

## Slide 134: MindSphere API Asset Management Service
Base endpoint methods
GET: /api/assetmanagement/v3/assets
Purpose:
Read Assets
Filter Assets
Get Asset Children
Get Asset Details
Read the tenant‘s assets and their details, and
navigate through the hierarchy

## Slide 135: MindSphere API Asset Management Service
Roles / Scopes
Role | Description
mdsp:core:assetmanagement.admin | Admin role allows users to create, read, update or delete assets, asset types, aspect types and files in Asset Management Service
mdsp:core:assetmanagement.standarduser | StandardUser role allows users to read or update assets and files, and to read asset types and aspect types in Asset Management Service
mdsp:core:assetmanagement.reporter | Reporter role allows users to read assets, asset types, aspect types and files in Asset Management Service
mdsp:core:assetmanagement.subtenantuser | SubTenantUser role allows users to read asset- and aspect types, read or update assets, and read, update or delete files in Asset Management Service

## Slide 136: MindSphere API Asset Management Service
Get all assets - Request
GET /api/assetmanagement/v3/assets
Read all asset for the logged in tenant.
Parameter Name | Description | Example | Optional
- | - | - | -
No parameters required:

## Slide 137: MindSphere API Asset Management Service
Get all assets – positive Response
{ "_embedded": {
"assets": [
{
"assetId": "7e2f0e528e204c41bd5a503e1a94cd62",
"tenantId": "academy2",
"name": "Democase_Location",
"etag": 2,
"externalId": null,
"t2Tenant": null,
"description": "Democase with a PLC and 3 Data Points",
"parentId": "555a9bfdd7b94ade8116992f56807c0d",
"typeId": "academy2.democase1",
"location": {
"country": "",
"region": "",
"locality": "Erlangen",
"streetAddress": "Schuhstr. 60",
"postalCode": "91052",
"longitude": 11.008239,
"latitude": 49.589216
},
"variables": [],
"aspects": [],
"_links": {
<HAL INFORMATION>
}
}, <NEXT ASSET>
]
}}
truncated! there may follow more children with the same format like above

## Slide 138: MindSphere API Asset Management Service
Get all assets – positive Response
{ "_embedded": {
"assets": [
{
"assetId": "7e2f0e528e204c41bd5a503e1a94cd62",
"tenantId": "academy2",
"name": "Democase_Location",
"etag": 2,
"externalId": null,
"t2Tenant": null,
"description": "Democase with a PLC and 3 Data Points",
"parentId": "555a9bfdd7b94ade8116992f56807c0d",
"typeId": "academy2.democase1",
"location": {
"country": "",
"region": "",
"locality": "Erlangen",
"streetAddress": "Schuhstr. 60",
"postalCode": "91052",
"longitude": 11.008239,
"latitude": 49.589216
},
"variables": [],
"aspects": [],
"_links": {
<HAL INFORMATION>
}
}, <NEXT ASSET>
]
}}
truncated! there may follow more children with the same format like above
HAL links section, importand are parent, children, aspects, events …
"self": {
"href": "https://<mdsp-url>/api/assetmanagement/v3/assets/7e2f0e528e204c41bd5a503e1a94cd62"
},
"parent": {
"href": "https://<mdsp-url>/api/assetmanagement/v3/assets/555a9bfdd7b94ade8116992f56807c0d"
},
"aspects": {
"href": "https://<mdsp-url>/api/assetmanagement/v3/assets/7e2f0e528e204c41bd5a503e1a94cd62/aspects"
},
"location": {
"href": "https://<mdsp-url>/api/assetmanagement/v3/assets/7e2f0e528e204c41bd5a503e1a94cd62/location"
},
"variables": {
"href": "https://<mdsp-url>/api/assetmanagement/v3/assets/7e2f0e528e204c41bd5a503e1a94cd62/variables"
}

## Slide 139: MindSphere API Asset Management Service
GET /api/assetmanagement/v3/assets
Find Assets
Parameter Name | Description | Example | Mandatory
size | Specifies the number of elements in a page. Default is 10 | 100 | No
page | Specifies the requested page index. Default is 0 | 0 | No
filter | Specifies the additional filtering criteria | see next slide | No
sort | Specifies the ordering of returned elementsAppend ,asc or ,desc for sorting direction. Default is timestamp descending order | status,asc | No

## Slide 140: MindSphere API Asset Management Service
GET /api/assetmanagement/v3/assets?filter=<filter>
Find Assets
Parameter Name | Description | Examples | Mandatory
filter | Supports all basic fields. Complex filtering possible. | {"typeId": "core.mcnano"} {"name": {"startsWith": {"value": "MCN"}}} | No

## Slide 141: MindSphere API Asset Management Service
Or and And
Find Assets – Examples
Filter by tenantId and type:
GET /api/assetmanagement/v3/assets?filter={"tenantId":"academy2", "typeId":"core.mcnano"}
Search in the name:
GET /api/assetmanagement/v3/assets?filter={"name": {"contains": {"value": "MCN"}}}
GET /api/assetmanagement/v3/assets?filter={
"typeId": {
"or": [
{"eq": "core.mcnano" },
{"eq": "core.mclib" }]},
"parentId": "864e19ddf02b49f48f96244258a83e16"
}

## Slide 142: MindSphere API Asset Management Service
GET /api/assetmanagement/v3/assets/root
Read the asset root of the logged-in tenant. This is the first asset in the hierarchy.
Get root asset
Parameter Name | Description | Example | Mandatory
- | - | - | -

## Slide 143: MindSphere API Asset Management Service
GET /api/assetmanagement/v3/assets/{id}
Get details for one asset. Response content is similar to the requests shown before.
Get details for an asset
Parameter Name | Description | Example | Mandatory
id | Asset id of the asset you want to read the details for | 7e2f0e528e204c41bd5a503e1a94cd62 | Yes

## Slide 144: MindSphere API IoT Time Series Service
Demo
Use the Postman Collection to investigate this API

## Slide 145: MindSphere API - Asset Management Service Summary
How do we read information of the asset?
There are several endpoints depending on the type of asset information requested
How can we navigate through the asset hierarchy?
The HAL structure tells from where to request e.g. parent and further information

## Slide 146
MindSphere
Pump application

## Slide 147: Architecture & API Learning Goals
How to call and use MindSphere APIs
MindSphere API Roles
Angular basics and application Structure
Exercise
Learn to develop your first application

## Slide 148: What do we want to do?

## Slide 149: How do we do this?
Angular as frontend framework - https://angular.io/
Nodejs & npm (node package manager)
TypeScript
HTML
CloudFoundry
MindSphere APIs
  Asset Management Service
  IoT Time Series Aggregates Service
  Event Management Service
Our pump asset

## Slide 150: MindSphere
How do I call a MindSphere API from a frontend application?

## Slide 151: What do we want to do?
myUi
FrontendApplication
Session cookie
MindSphere Gateway
/api/assetmanagement/v3/assets
MindSphere Core APIs
AssetManagement
IOT
EventManagement
...

## Slide 152: Direct MindSphere API calls from a frontend applicaton
All MindSphere API are available via a relative url call: /api/...
/api/ is a reserved keyword (can't be used in your own app)
In this way the authorization information is stored in a session cookie
For example:
  https://academy2-frontendtb-academy2.eu1.mindsphere.io /api/assetmanagement/v3/assets/root

## Slide 153: MindSphere API roles
The application needs the right to access MindSphere APIs
Each MindSphere API provides a set of API core roles
In developer cockpit, you need to add the needed core roles to your application

## Slide 154: Angular basics
Components
  Multiple components build together a screen of an application
  One component is the starting point for the application
Templates
  View part of the application (HTML)
  Data can be added via Data binding
Services
  Implements the application logic (in our case the communication with MindSphere APIs)
Dependency injection
  Components consume services, a.k.a. Injection

## Slide 155: Application structure
MindSphere APIs
service
service
service
Injector
app.component
section.overview
components…
section.data
components…
section.maintenance
components…

## Slide 156: Folder structure
Section
Component
Service

## Slide 157: Angular commands
Install angular packages:
npm install
Run angular locally:
npm start
Build distribution package (before cf push):
npm run build:prod

## Slide 158: My Pump Application
Exercise
Install angular, build application & push application

## Slide 159: Exercise: Install angular, build application & push application
Goto folder 050-pump-app-overview
npm install
npm run build:prod
cf push
Register the application
Complete the sourcecode (only in service file)
  Folder: \src\app\sections\overview\services
  File: overview-mindsphere.service.ts
  Change assetId in \src\app\services\asset-id.service.ts

## Slide 160: Content Security Policy (CSP)
Content Security Policy (CSP) is a way to mitigate for example Cross Site Scripting (XSS) attacks.
MindSphere uses a Whitelist approach
The default policy is very strict
Content-Security-Policy:
default-src 'self' static.{env}.{mindsphere-domain};
style-src * 'unsafe-inline';
script-src 'self' 'unsafe-inline' static.{env}.{mindsphere-domain};
img-src * data:;

## Slide 161: Change CSP header in Developer cockpit

## Slide 162: My Pump Application
Exercise
Add the font-src to the CSP header of your application
font-src fonts.gstatic.com static.eu1.mindsphere.io;

## Slide 163: Howto update data
(Some) MindSphere APIs use Optimistic concurrency control to prevent simultaneous updates from multiple sources
Process
Read the field etag from the response
Apply the content of the etag field to the PUT request as header field "If-Match"

## Slide 164: My Pump Application
Exercise
Implement the update part in your application

## Slide 165: Architecture & API Summary
What do we need for building an MindSphere Application?
Angular, NodeJS and npm, TypeScript, HTML, CloudFoundry, MindSphere APIs.

## Slide 166
MindSphere
IoT Time Series API

## Slide 167: IoT Time Series API Learning Goals
Search endpoint
Result structure
Create or update data
Delete data
How can we search for raw data
&
how can we create or update data?
Notes: Go through the agenda of today’s training with explanation for each item
MSPH Ecosystem -> How does it look like & what parts do exist in the MSPH ecosystem?
MSPH Scalable Portfolio -> What does MSPH currently offer (e.g. infrastructure, APIs, apps)?
IT security -> How do we make sure your data is safe and no one has unauthorized access to your data?
Demonstration/Hands-On -> Probably most interesting part as we onboard a device to MSPH and let actually a training participant connect the device with MSPH
Use Cases - MindApps & Connectivity -> For which use cases can MindSphere be used or is being used already? What are the benefits for our customers?
MSPH Pricing Model -> Chapter to illustrate the costs which will be something most participants want to know
MSPH forums and networks -> How do I as a customer get in touch, e.g. to get help or answers to general questions?

## Slide 168: MindSphere API IoT Time Series API
Basic Endpoint
/api/iottimeseries/v3/timeseries
Purpose:
Retrieve raw data
Filter on time range
Filter specific aspect values
Investigate on raw data
Write your own analytics
Export
Don‘t mix with aggregated
time series methods

## Slide 169: MindSphere API IoT Time Series Service
Roles / Scopes
Role | Description
mdsp:core:iot.timUser | Granting read access to time series.
mdsp:core:iot.timAdmin | Granting read, write and delete access to time series.

## Slide 170: MindSphere API IoT Time Series Service
Endpoints
Request Method | Description | End Point
GET | /iottimeseries/v3/timeseries | Query time series data with a precision of 1 millisecond

## Slide 171: MindSphere API IoT Time Series Service
Parameter Name | Description | Example | Mandatory
from | Beginning of the time range to read (exclusive) | 2018-01-31T00:00:00Z | No
to | End of the time range to read (inclusive) | 2018-01-31T20:00:00Z | No
limit | maximum number of entries to read | 1 | No
select | select fields to return | Temperature | No
sort | sort order (asc or desc, default: asc) | desc | No
Get timeseries
GET /api/iottimeseries/v3/timeseries/{entity}/{propertyset}
Asset-Id
Aspect-Name
Notes: Read time series data for a single entity and propertyset. Returns data for a specified time range. Returns the latest value if no range is provided.

## Slide 172: MindSphere API IoT Time Series Service
Get raw timeseries
Response (Body)
[
{
"_time": "2018-02-22T00:50:10.607Z",
"sin1": 25.815107,
"sin2": -44.914648427989135,
},
{
"_time": "2018-02-22T00:50:25.614Z",
"sin1": 30.61933,
"sin2": -44.454259707516634,
}
]
Paging is implemented as a header called "link" (see RFC 5988)
link →<https://gateway.eu1.mindsphere.io/api/iottimeseries/v3/timeseries/01c3636d75f242cb828af1a87e1a1860/Sensors?from=2018-12-01T05:33:13.332Z&limit=2000&to=2018-12-10T23:50:00Z>; rel="next"
Returns maximum 2000 records in a response

## Slide 173: MindSphere API IoT Time Series Service
Endpoints
Request Method | Description | End Point
PUT | /api/iottimeseries/v3/timeseries | Write or update time series data for a single entity and propertyset.
Notes: Existing time series data is overwritten. Data for all properties within a propertyset needs to be provided together.
Restrictions¶
Multiple records for an entity instance and property set can be written in one call to the service. The maximum size of a write payload is 1 megabyte.
When writing or deleting data, the default behavior of the service is to queue the incoming request and perform the physical writes to the underlying data store asynchronously. In this mode, if a user writes time series data and immediately tries to read it back, it may not yet be present in the data store and it won't be returned. If a user deletes data and then reads that time range, the data may not have been physically deleted yet, and could be returned in the response. Requests for an asset (entity) sent in queued mode will be processed in the order they were received.

## Slide 174: MindSphere API IoT Time Series Service
Parameter Name | Description | Example | Mandatory
entity | unique identifier of the entity | b75549b996014c60809902662df158c7 | Yes
propertyset | name of the propertyset | simulation | Yes
body | timeseries data | see next slide | Yes
Create or update timeseries
PUT /api/iottimeseries/v3/timeseries/{entity}/{propertyset}
Notes: Existing time series data is overwritten. Data for all properties within a propertyset needs to be provided together.

## Slide 175: MindSphere API IoT Time Series Service
Create timeseries
Request (Body)
[
{
"_time": "2018-02-22T00:50:10.607Z",
"sin1": 25.815107,
"sin2": -44.914648427989135,
},
{
"_time": "2018-02-22T00:50:25.614Z",
"sin1": 30.61933,
"sin2": -44.454259707516634,
}
]

## Slide 176: MindSphere API IoT Time Series Service
Endpoints
Request Method | Description | End Point
DELETE | /api/iottimeseries/v3/timeseries | Delete time series data for a single entity and propertyset within a given time range
Notes: Only 6 months of data can be deleted at a time.

## Slide 177: MindSphere API IoT Time Series Service
Parameter Name | Description | Example | Mandatory
from | Beginning of the time range to read (exclusive) | 2018-01-31T00:00:00Z | Yes
to | End of the time range to read (inclusive) | 2018-01-31T20:00:00Z | Yes
Delete timeseries
DELETE /api/iottimeseries/v3/timeseries/{entity}/{propertyset}
Status Code 204 (No Content)
Notes: Only 6 months of data can be deleted at a time.

## Slide 178: MindSphere API IoT Time Series Service
Demo
Use the Postman Collection to investigate this API

## Slide 179: IoT Time Series API Summary
How can we search for raw data?
GET request on the endpoint
How can we create or update data?
DELETE or PUT request on the endpoint

## Slide 180
MindSphere
IoT Time Series Aggregates Service

## Slide 181: Aggregate Services Learning Goals
Use Aggregate Service
How can we fetch timeseries data efficiently for visualization from MindSphere?

## Slide 182: MindSphere API Aggregate Service
Retrieving aggregated data
Precalculated aggregates
Aggregation according to various values e.g.: min, max, first, last, count
Retrieve aggregated timeseries data suitable for e.g., visualization
For running analyses, use timeseries raw data instead!

## Slide 183: MindSphere API Aggregate Service
Endpoints
Request Method | Description | End Point
GET | /api/iottsaggregates/v3/aggregates | Aggregated timeseries with an assortment summary of information

## Slide 184: MindSphere API Aggregate Service
Roles / Scopes
Role | Description
mdsp:core:iot.tsaUser | Granting access to time series aggregates.

## Slide 185: MindSphere API Aggregate Service
Aggregated Data
… is available in precalculated intervals
… supports the following intervals
… should be an exact multiple of a precalculated aggregation interval (for best performance)
… is wall clock aligned
… is created based on arrival of data and time logic
Returned data
2 minute | 1 hour | 1 day
1-120 seconds | 1-60 minutes | 1-24 hours | 1+ days | 1+ weeks | 1+ months
minimum value | maximum value | average | sum | count | first value | last value
Notes: Intervals smaller than the smallest precalculated interval are also available and generated on the fly (future release). Intervals equal to or larger than the smallest precalculated interval are only available as multiples of precalculated intervals.
Each aggregated record contains an assortment summary of information,
including first value and time of first value of the interval
last value and time of last value of the interval
minimum value and time of the minimum value during the interval
maximum value and time of the maximum value during the interval
the count of the values during the interval
the sum of the values during the interval
and the average of the values during the interval.
The aggregated data is wall clock aligned.
two-minute data will end at two minutes after the hour, four minutes after the hour, and so on.
hourly data will end at the top of the hour.
daily data will end at midnight in UTC for this developer release.
The data summarized in an aggregated interval is the data with time stamps greater than the start time of the interval and less than or equal to the end time of the interval. This ensures that count type of data is correctly reflected in the aggregated interval. For example, if a device provides a wall clock aligned count at the end of each five minutes, an hourly aggregation will include the data with time stamps from five minutes after the hour until the end of the hour (3:05 to 4:00 for example).
Aggregates are created based on arrival of data and time logic.
two-minute aggregated data is created within two minutes after the two-minute interval has finished.
hourly data is created within eight minutes after the end of the hour.
daily data is created within fifteen minutes after midnight in UTC time for this release.
Aggregated data is only created if time series data exists for that period. Aggregates are created based on the data that is available at the time. Late arriving data will not be included in the initial aggregated results, but will trigger a recalculation after a delay.

## Slide 186: MindSphere API Aggregate Service
Aggregated Data
1 hour interval
5:00 – 10:00
60-minute interval
5:30 – 10:30
an interval duration of 1 week must start and end on a Monday
An interval duration of 7 days could start on any day of the week
two-minute aggregated data is created within two minutes after the two-minute interval has finished
hourly data is created within eight minutes after the end of the hour
daily data is created within fifteen minutes after midnight in UTC time for this release
Notes: Intervals smaller than the smallest precalculated interval are also available and generated on the fly (future release). Intervals equal to or larger than the smallest precalculated interval are only available as multiples of precalculated intervals.
Each aggregated record contains an assortment summary of information,
including first value and time of first value of the interval
last value and time of last value of the interval
minimum value and time of the minimum value during the interval
maximum value and time of the maximum value during the interval
the count of the values during the interval
the sum of the values during the interval
and the average of the values during the interval.
The aggregated data is wall clock aligned.
two-minute data will end at two minutes after the hour, four minutes after the hour, and so on.
hourly data will end at the top of the hour.
daily data will end at midnight in UTC for this developer release.
The data summarized in an aggregated interval is the data with time stamps greater than the start time of the interval and less than or equal to the end time of the interval. This ensures that count type of data is correctly reflected in the aggregated interval. For example, if a device provides a wall clock aligned count at the end of each five minutes, an hourly aggregation will include the data with time stamps from five minutes after the hour until the end of the hour (3:05 to 4:00 for example).
Aggregates are created based on arrival of data and time logic.
two-minute aggregated data is created within two minutes after the two-minute interval has finished.
hourly data is created within eight minutes after the end of the hour.
daily data is created within fifteen minutes after midnight in UTC time for this release.
Aggregated data is only created if time series data exists for that period. Aggregates are created based on the data that is available at the time. Late arriving data will not be included in the initial aggregated results, but will trigger a recalculation after a delay.

## Slide 187: MindSphere API Aggregate Service
Parameter Name | Description | Example | Mandatory
from | Beginning of the time range to read | 2018-01-31T00:00:00Z | Yes
to | End of the time range to read | 2018-01-31T20:00:00Z | Yes
intervalValue | Interval duration for the aggregates in intervalUnits | 1 | Yes
intervalUnit | Interval duration unit for the aggregates | hour | Yes
select | Properties and fields to select | Temperature | No
Get aggregated timeseries
GET /api/iottsaggregates/v3/aggregates/{entity}/{propertyset}
select parameter can be used to select certain fields with variableName.fieldName
Asset-Id
Aspect-Name

## Slide 188: MindSphere API Aggregate Service
Get aggregated timeseries
Response (Body)
[{ "Memory": {
"minvalue": 3236,
"maxvalue": 3554,
"mintime": "2018-01-31T02:50:00Z",
"maxtime": "2018-01-31T00:10:00Z",
"firstvalue": 3554,
"lastvalue": 3301,
"firsttime": "2018-01-31T00:10:00Z",
"lasttime": "2018-01-31T04:00:00Z",
"average": 3320.125,
"sum": 79683,
"countuncertain": 0,
"countbad": 0,
"countgood": 24
},
"starttime": "2018-01-31T00:00:00Z",
"endtime": "2018-01-31T04:00:00Z"
}]
Returns maximum 200 records in a response

## Slide 189: MindSphere API Aggregate Service
Use the Postman Collection to investigate this API
Demo

## Slide 190: Exercise: Install angular, build application & push application
Goto folder 060-pump-app-timeseries
npm install
npm run build:prod
cf push
Complete the sourcecode (only in service file)
  Folder: \src\app\sections\data\services
  File: data-mindsphere.service.ts
  Change assetId in \src\app\services\asset-id.service.ts

## Slide 191: Aggregate Service Summary
How can we fetch timeseries data efficiently for visualization from MindSphere?
With Aggregate Service we can reduce the amount of data points.

## Slide 192
MindSphere
Event Management Service

## Slide 193: MindSphere API – Event Management Service Learning Goals
Event data structure
Request end points
Read and write data
How can we view and create events in MindSphere?

## Slide 194: MindSphere API – Event Management Service Overview
Representation of events that occur associated to assets E.g. a measured characteristic of an equipment has reached a threshold indicating a failure
Display Events in your app
Acknowledge events in your app and change their status in MindSphere accordingly
Create new events
Tasks:
  Retrieve events
  Store events
  Modify events
  Understand event types

## Slide 195: MindSphere API Event Management Service
Event type hierarchy
BaseEvent
MindSphereAspectPropertyEvent
MindSphere RuleEvent
MindSphere StandardEvent
MindSphere CustomEvent
timestamp
typeId
correlationId
entityId
source
code
acknowledged
description
severity
ruleId
property
Notes: Event types can be derived from other (parent) event types. An inheritance hierarchy of up to 4 levels is allowed. Every event type inherits all fields from their ancestor event types.

## Slide 196: MindSphere API Event Management Service
Event types
are assigned to a custom event
define a set of custom fields representing additional properties of the custom event
custom fields have a data type and can be defined as required and filterable
inheritance hierarchy of up to 4 levels
Scope: global or local
TTL: time to live (after this number of days the event will be automatically deleted)

## Slide 197: MindSphere API Event Management Service
Roles / Scopes
Role | Description
mdsp:core:em.eventmanager | Role granting access to manage everything in eventmanagement system
mdsp:core:em.eventcreator | Role granting access to create events (create, read and update) in eventmanagement system
mdsp:core:em.eventviewer | Role granting access to read events and eventTypes in eventmanagement system

## Slide 198: MindSphere API Event Management Service
Standard event data structure
{
"id": "9f3795fb-dfa3-447b-936c-a63f716d2686",
"typeId": "b7f9a843-a530-4159-989e-20645e2b647d",
"correlationId": "85ba8d01-f831-4354-94d0-354759e91de5",
"timestamp": "2018-02-01T11:00:00Z",
"entityId": "b75549b996014c60809902662df158c7",
"etag": 0,
"_links": {
"self": {
"href": "<base-url>/api/eventmanagement/v3/events/9f3795fb-dfa3-447b-936c-a63f716d2686"
}
},
"severity": 30,
"code": "",
"acknowledged": false,
"description": "Memory high",
"source": "Manual"
}
Internal ID, required for retrieving/updating a specific event

## Slide 199: MindSphere API Event Management Service
Endpoints
Request Method | Endpoint | Description
GET | /api/eventmanagement/v3/events | Find events based on a request filter
GET | /api/eventmanagement/v3/events/{eventId} | Get a specific event
POST | /api/eventmanagement/v3/events | Create a new event
PUT | /api/eventmanagement/v3/events/{eventId} | Update an existing event

## Slide 200: MindSphere API Event Management Service
Find Events
GET /api/eventmanagement/v3/events
Parameter Name | Description | Example | Mandatory
size | Specifies the number of elements in a page. Default is 20 | 100 | No
page | Specifies the requested page index. Default is 0 | 0 | No
filter | Filter parameter | {"severity": 1} | No
sort | The order in which the elements are returned. Specify status, severity or timestamp for the field to sort by. Append ,asc or ,desc for sorting direction. Default is timestamp descending order | status,asc | No

## Slide 201: MindSphere API Event Management Service
Filter by entityId ("Asset)":
GET /api/eventmanagement/v3/events?filter={"entityId": "b75549b996014c60809902662df158c7"}
Filter by timestamp:
GET /api/eventmanagement/v3/events? filter={"timestamp": {"between":"[2018-01-31T00:00:00Z,2018-01-31T23:59:59Z]"}}
Get all events:
GET /api/eventmanagement/v3/events
Find Events – Examples
Notes: If timestamp is not provided in the filter, the events from the 7 days will be filtered for by default.
Multiple typeId expressions (by using and, or logical operators) in filter parameter is not allowed. Only equality function is supported on it.
Filtering with typeId having BaseEvent is not supported. If typeId is missing from filter expression then MindsphereStandardEvent typed (including) descendants - polymorphic query) events will be returned.
Negation of typeId in filter expression is not allowed.
If there are multiple events that have the same correlationId and entityId then only the latest one will be present in the returning list of events.

## Slide 202: MindSphere API Event Management Service
Get an Event by ID
Example:
GET /api/eventmanagement/v3/events/fa884d56-0570-4e0c-8c12-dbcc8e7c780c
GET /api/eventmanagement/v3/events/{eventId}

## Slide 203: MindSphere API Event Management Service
Example request (body):
POST /api/eventmanagement/v3/events
{
"typeId": "com.siemens.mindsphere.eventmgmt.event.type.MindSphereStandardEvent",
"timestamp": "2018-01-31T11:00:00.000Z",
"entityId": "b75549b996014c60809902662df158c7",
"severity": 1,
"description": "Test event via API call",
"code": "TestCode01",
"acknowledged": false
}
Create a new Event

## Slide 204: MindSphere API Event Management Service
{
"id": "60d73e4e-5aac-4098-bb87-2be0577f8a66",
"typeId": "com.siemens.mindsphere.eventmgmt.event.type.MindSphereStandardEvent",
"correlationId": "0ccd7c42c0114dde8ed199f9bef64fe6",
"timestamp": "2018-01-31T11:00:00Z",
"entityId": "b75549b996014c60809902662df158c7",
"severity": 1,
"code": "TestCode01",
"acknowledged": true,
"description": "Test event via API call"
}
PUT /api/eventmanagement/v3/events/{eventId}
Example request (body):
Update an existing event
Notes: "message": "Following fields cannot be updated: correlationId, timestamp, entityId."

## Slide 205: MindSphere API Event Management Service
{
"typeId": "com.siemens.mindsphere.eventmgmt.event.type.MindSphereStandardEvent",
"correlationId": "0ccd7c42c0114dde8ed199f9bef64fe6",
"timestamp": "2018-01-31T11:00:00Z",
"entityId": "b75549b996014c60809902662df158c7",
"severity": 1,
"code": "TestCode01",
"acknowledged": false,
"description": "Test event via API call"
}
POST /api/eventmanagement/v3/events
Example request (body):
The original event remains in the database and a new event is created with the same entityId and correlationId but a different id
Add historical data to an existing event
Listing events will return only the latest of an event's history. But we can list the whole history of the event with 'history' query parameter set to true.
Notes: Updating¶
Standard events can be updated. There are two ways to update an event: With a PUT request we overwrite an event and with a POST request a history is created.
This means the original event remains in the database and a new event is created with the same entityId and correlationId but a different id.
Listing events will return only the latest of an event's history.

## Slide 206: MindSphere API Event Management Service
Endpoints for bulk create events
Request Method | Endpoint | Description
POST | /api/eventmanagement/v3/createEventsJobs | Create events (asynchronous)
GET | /api/eventmanagement/v3/createEventsJobs/{jobId} | Get a information about a create job

## Slide 207: MindSphere API Event Management Service
Example request (body):
POST /api/eventmanagement/v3/createEventsJobs
{
"events": [
{
"typeId": "com.siemens.mindsphere.eventmgmt.event.type.MindSphereStandardEvent",
"timestamp": "2018-07-06T11:01:00.000Z",
"entityId": "b43703b007924c2889adc9da9f818a5b",
"severity": 1,
"description": "TB Bulk event 1",
"code": "tbe1",
"acknowledged": false
},
[...]
]
}
Create events
Result:
{
"id": "566a320e-c762-42f0-86c4-6249b0eedc27",
"state": "ACCEPTED"
}

## Slide 208: MindSphere API Event Management Service
Example response:
GET /api/eventmanagement/v3/createEventsJobs/{jobId}
{
"id": "ce464d4f-59a7-4bb3-815b-9b70fe3931ac",
"state": "FINISHED",
"details": {
"resultDescription": [
[...]
]
}
}
Create events (check status)

## Slide 209: MindSphere API Event Management Service
Endpoints for deleting events
Request Method | Endpoint | Description
POST | /api/eventmanagement/v3/deleteEventsJobs | Delete events (asynchronous)
GET | /api/eventmanagement/v3/deleteEventsJobs/{jobId} | Get a information about a delete job

## Slide 210: MindSphere API Event Management Service
Example request (body):
POST /api/eventmanagement/v3/deleteEventsJobs
{
"filter": {
"typeId": "com.siemens.mindsphere.eventmgmt.event.type.MindSphereStandardEvent",
"timestamp": {"between":"[2018-06-10T03:24:41.052Z,2018-06-22T23:59:59Z]"}
}
}
Delete events
Result:
{
"id": "566a320e-c762-42f0-86c4-6249b0eedc27",
"state": "ACCEPTED"
}

## Slide 211: MindSphere API Event Management Service
Example response:
GET /api/eventmanagement/v3/deleteEventsJobs/{jobId}
{
"id": "566a320e-c762-42f0-86c4-6249b0eedc27",
"state": "FINISHED",
"details": {
"resultCode": "200",
"resultDescription": "18482 events deleted."
}
}
Delete events (check status)

## Slide 212: MindSphere API Event Management Service
Endpoints for Event Types
Request Method | Endpoint | Description
GET | /api/eventmanagement/v3/eventTypes | Find events based on a request filter
GET | /api/eventmanagement/v3/eventTypes/{eventId} | Get a specific event type
POST | /api/eventmanagement/v3/eventTypes/ | Create a new event type

## Slide 213: MindSphere API Event Management Service
Find Event Types
GET /api/eventmanagement/v3/eventTypes
Parameter Name | Description | Example | Mandatory
size | Specifies the number of elements in a page. Default is 20 | 100 | No
page | Specifies the requested page index. Default is 0 | 0 | No
filter | Filter parameter: id, name, owner, scope | {"owner": "academy2"} | No
sort | Sorting field Append ,asc or ,desc for sorting direction. Default is name ascending order | id,asc | No

## Slide 214: MindSphere API Event Management Service
Example request (body):
POST /api/eventmanagement/v3/eventTypes
{ "name": "MindSphereAcademyTrainingEvent",
"ttl": 7,
"scope": "LOCAL",
"parentId": "com.siemens.mindsphere.eventmgmt.event.type.BaseEvent",
"fields": [{
"name": "courseId",
"filterable": true,
"required": true,
"updatable": true,
"type": "STRING"
}]
}
Create a new event type

## Slide 215: MindSphere API Event Management Service
Restriction for event types
Field | Restriction
ttl | max. 1825 (5 years)
name of the event type | max. 64 characters
field name | max. 64 characters
number of fields | max. 100
inheritance depth | max. 4
filterable fields | max. 10

## Slide 216: MindSphere API Event Management Service
Demo
Use the Postman Collection to investigate this API

## Slide 217: MindSphere API – Event Management Service Summary
How can we view and create events in MindSphere?
Use Event Management Service for getting the state of the assets

## Slide 218
MindSphere
Frontend/Backend

## Slide 219: Frontend/Backend Learning Goals
Role of MindSphere Gateway
Authentication & Authorization
Example with source code
Learn the concept of how the backend and frontend of an application interacts.

## Slide 220: What do we want to do?
myUi
Frontend-Application
Session Look
MindSphere Gateway
MindSphere Core APIs
AssetManagement
IOT
EventManagement
...
myService
Backend-Application

## Slide 221: What do we need to do?
myService
Backend-Application
myUi
Frontend-Application
MindSphere Gateway
MindSphere Core APIs
AssetManagement
IOT
EventManagement
...
/service/maintenance/entry
JWT in Authorization header
JWT in Authorization header

## Slide 222: MindSphere - Authentication & Authorization General
MindSphere 3.0 authentication & authorization is based on OAuth 2.0
OAuth 2.0 is a standard protocol for authorization, defined in misc. RFCs (details see https://oauth.net/2/)
One part of the definiton are: JSON Web Token (JWT)

## Slide 223: MindSphere - Authentication & Authorization JSON Web Token
JSON Web Token / JWT
Open standard (defined in RFC 7519) for access token for different claims
Important fields
  iss: issuer
  aud: audience
  exp: expiration time
  iat: issued at time
  scope

## Slide 224: Source code example

## Slide 225: MindSphere Application components

## Slide 226: Exercise
Extend your frontend application with a backend and create events from there
Exercise

## Slide 227: Exercise
Task: Extend your frontend application with a backend and create events from there
Create a combined manifest.yml
Push both parts of your application
Register the second component
Run the application
Build a call from the frontend to the backend

## Slide 228: Frontend/Backend Summary
How do you extend your frontend application with a backend and create events from there?
By creating a combined manifest.yml, push both parts of your app and register the second component.

## Slide 229: MindSphere Documentation
Developer documentation at www.mindsphere.io/developer
User documentation at www.mindsphere.io/documentation
Code examples
Tutorials
API description
Getting connected to MindSphere
API references
Developer Cockpit
How to use Asset Management
How to Use FleetManager
How to Operator Cockpit
How to use Developer Cockpit
UI Elements
Connectivity
App example
SDKs

## Slide 230: MindSphere Connect to Us
Website | www.mindsphere.io
MindSphere Community | https://community.plm.automation.siemens.com/t5/MindSphere/ct-p/MindSphere
MindSphere General | contact@mindsphere.io
MindSphere Support Team | Call Center: +49 (0)911 895 7 272 (Germany) Online Support: http://www.siemens.com/automation/service&support Support Request: http://www.siemens.com/automation/support-request
MindSphere Academy | training@mindsphere.io
MindSphere Status | status.mindsphere.io